## Slide 1: Chapter 2 Logical algebra
2.1 Three Basic Functions of Logical Algebra
2.2 Laws and Rules of Logical Algebra
2.3 Function Transformation
2.4 Function Simplification

## Slide 2
AND: logical multiplication
OR: logical addition
NOT: logical inverter
2.1 Three basic functions of
logical algebra

## Slide 3
Truth Table
1 1 1
1 0 0
0 1 0
0 0 0
A B F
Function Table
A B F
off off off
off on off
on off off
on on on
F
E
A
B
switch
power
supply
light
(1) “AND” function

## Slide 4
F＝f(A，B)=A·B＝AB
A
B
F
Logic gate of “AND” (hardware symbol)
If all conditions are met, the event will occur.
It is named as logical multiplication (AND).
Logic function of “AND”

## Slide 5
1 1 1
1 0 1
0 1 1
0 0 0
A B F
Truth Table
on
on
on
Function Table
A B F
off off
off on
on off
on on
off
F
E
A
B
switch
power
supply
light
(2) “OR” function

## Slide 6
F＝f(A，B)＝A＋B
A
B
F
Logic gate of “OR” (hardware symbol)
Logic function of “OR”
If one condition is met, the event will occur.
It is named as logical addition (OR).

## Slide 7
F
E
A
R
1 0
0 1
A F
Truth Table
Function Table
A F
off on
on off
switch
power
supply
light
resistor
(3) “NOT” function

## Slide 8
A
F=A
Logic gate of “NOT” (hardware symbol)
Logic function of “NOT”
F＝A
The input and output are inverting.
It is named as logical inverter (NOT).

## Slide 9: 2.2.1 Laws of logical algebra
(1) Laws of 0 and 1 (axioms)
2.2 Laws and Rules of Logical Algebra

## Slide 10
(3) Commutative Law
(2) Laws of single variable (theorems)

## Slide 11
(4) Associative Law
(5) Distributive Law
A(BC)=(AB)C=(AC)B
A+(B+C)=(A+B)+C=(A+C)+B
A(B+C)=AB+AC
A+BC=(A+B)·(A+C)
Proof: R.H.S. of Eq.=AA+AC+AB+BC=A+AC+AB+BC
=A(1+C+B)+BC=A+BC=L.H.S. of Eq.
distributive law of multiplication
distributive law of addition

## Slide 12
(6) De Morgan’s Law
Proof by truth table:
0 0 0 1 1 1 1
0 1 0 1 1 0 1
1 0 0 1 0 1 1
1 1 1 0 0 0 0

## Slide 13: Exercise
Prove the equation by truth table.

## Slide 14
(7) The other commonly used laws
redundancy law
appending law
①
②
③
④
⑤
There are three product terms. The first two product terms contain the inverted variables A and A NOT. The third term contains the rest variables from the first two terms. The third term is redundant.

## Slide 15
Proof:
A+BC=(A+B)·(A+C) distributive law of addition
①
②
③
Proof:
Proof:

## Slide 16
A+BC=(A+B)·(A+C) distributive law of addition
④
Proof:

## Slide 17
R.H.S. of Eq.
L.H.S. of Eq.=
L.H.S. of Eq.
R.H.S. of Eq.
Extension of redundancy law ⑤:
⑤
Proof:
Proof:

## Slide 18: 2.2.2 Rules of logical algebra
(1) Substitution Rule
Replace the variable with a function. Then the new expression is correct.
Replace
Example
Notes: Replace B with DC.
Apply the De Morgan’s Laws.

## Slide 19
De Morgan’s Laws
Replace B with more variables, and we get the general form of De Morgan's law:
Notes: Replace B with more variables, we get the general from of De Morgan’s law.

## Slide 20
(2) Inversion Rule
(we use it to write the inverse function.)

+
0 1
1 0
+
Exchange
Keep the operation order.
Notes: The inverse function is written as F NOT.
Exchange 0 and 1. Exchange plus and dot.
Exchange original variable and inverted variable.

## Slide 21
Example 1
Example 2
Example 3
Write the inverse function.
Notes: Exchange original variable and inverted variable. Exchange plus and dot.
In example 1 and example 3, add parentheses to keep the operation order.
In example 2, the big inverter is offset.

## Slide 22
(3) Duality Rule
(We use it to write the dual function.)
F(A，B，C )
FD(A，B，C )

0
1
1
0
+
+
A and are unchanged (keep the inverter).
Exchange
Keep the operation order.
Notes: The dual function is written as F-D

## Slide 23
(FD)D = F
(1) If an equation is correct, its dual form is also correct.
(2) If two functions are equal, their dual forms are also equal.
Properties of Duality Rule
(3) If we apply the duality rule on a function twice, we will obtain the original function.

## Slide 24
A+BC=(A+B)·(A+C)
F1=A+BC F2=(A+B)·(A+C)
Apply Duality Rule to get the dual function:
F1D=A(B+C)=AB+AC F2D=AB+AC
F1D= F2D
Let
F1=F2
Example: Use Duality Rule to prove the distributive law of addition.
Proof:
Then,
Notes: Prove the distributive law of addition.
Separate the left side and right side of the formula.
Apply the duality rule(exchange dot and plus).

## Slide 25
separate a variable, e.g., from F and expand F as follows:
(4) Expansion Rule (we use it to simplify function.)
F=f(X1,X2,···Xn)，
X1
If we have a logic function
Let to prove the above.
X1=0 or X1=1

## Slide 26: Exercise
Prove the expansion rule.
Let to prove the above.
X1=0 or X1=1

## Slide 29
Example: Simplify logic function by expansion rule.
Solution: (separate variable A)
Notes: Write A NOT dot. Replace A with 0 in the function.
Write A dot. Replace A with 1 in the function.
Variable A appears many times in function F.

## Slide 30: 2.2.3 Compound Functions
A
B
F
F＝AB
A
B
A
B
F
F＝A＋B
A
B
NAND
NOR
Logic gate
(hardware symbol)
Notes: NAND gate: AND gate is followed by inverter
NOR gate: OR gate is followed by inverter

## Slide 31
A
B
F
C
D
A
B
C
D
F=AB+CD
AND-OR-INVERTER
Logic gate
(hardware symbol)
Notes: Two AND gates, followed by OR gate, then followed by inverter.

## Slide 32
F
A
B
F
A
B
exclusive or
exclusive nor
OR: inclusive or
XOR
XNOR
Logic gate (hardware symbol)
Logic function
Notes: Operator of XOR: plus inside a circle
Operator of XNOR: dot inside a circle
XOR equals …, XNOR equals …

## Slide 33
XNOR：if A，B are equal, then F=1.
XOR：if A，B are unequal, then F=1.
How to understand XOR?
How to understand XNOR?
Notes: How to understand XOR?
How to understand XNOR?

## Slide 34
Truth Table
A B A B A B
0 0 0 1
0 1 1 0
1 0 1 0
1 1 0 1
If there are two inputs, the XOR result and the XNOR result are inverting.

## Slide 35
A B C
0 0 0 0 0
0 0 1 1 1
0 1 0 1 1
0 1 1 0 0
A B C
A B C
1 0 0 1 1
1 0 1 0 0
1 1 0 0 0
1 1 1 1 1
Truth Table
If there are three inputs, XOR and XNOR are equal.
Notes: If there are three inputs,

## Slide 36
A A=0 A A=1
1 A=A 0 A=A
0 A=A 1 A=A
1 1=0 0 0=1
0 0=0 1 1=1
1 0=0 1=1 0 1=1 0=0
A A=1 A A=0
Rules of XOR and XNOR
(1)
(2)
Treat A as 1. Treat A as 0.
Notes: If the two inputs are unequal, the xor result is 1.
If the two inputs are equal, the xnor result is 1.

## Slide 37
A B=B A A B=B A
(4) Associative Law
A (B C)=(A B) C
A (B C)=(A B) C
(3) Commutative Law
Notes: Commutative Law: we can exchange positions of A and B.
Associative Law: we can combine any two variables for calculation.

## Slide 38
=A+BC+BC=A+(B C)= Left
A+(B C)=(A+B) (A+C)
Right =(A+B) (A+C)+(A+B)(A+C)=ABC+A+BC
(5) Distributive Law
=ABC+ABC=A(B C)=Left
Right=ABAC+ABAC=AB(A+C)+AC(A+B)
A(B C)=AB AC
Notes: (1)Take AB as a whole. Take AC as a whole. Apply the De Morgan’s Laws. Remove parentheses. A and A NOT are offsetting.
Extract A. Write the XOR expression.
(2) Take parentheses as a whole. Apply the De Morgan’s Laws. Write A NOT once. Apply the distributive law of addition. A offsets A NOT. Write the XNOR expression.

## Slide 39
If A B=C, then A C=B or B C=A
If A B=C , then A C=B or B C=A
(6) Interchange Law
0 0 0
0 1 1
1 0 1
1 1 0
A B C
0 0 1
0 1 0
1 0 0
1 1 1
A B C
Notes: If exchange the input and output, the formula holds.
Prove it by truth table. Exchange input and output in the truth table.

## Slide 40: Exercise
Prove the interchange law by truth table.
If A B=C, then A C=B or B C=A
If A B=C , then A C=B or B C=A

## Slide 41
(7) Commonly Used Laws
A1 A2 An=
1 (odd number of “1s”)
0 (even number of “1s”)
1 (even number of “0s”)
A1 A2 An=
0 (odd number of “0s”)

## Slide 42
1
1
0
0
=
?
0
0
0
=
0
1
1
1
=
?
1
0
=
1
1
1
=
0
1
1
=
0
…...
odd number of “1s”
1
1
=
0
1
1
=
0
…...
even number of “1s”
A1 A2 An=
1 (odd number of “1s”)
0 (even number of “1s”)

## Slide 43
1
1
=
?
0
0
1
1
1
=
1
=
?
0
0
0
0
1
=
0
0
0
=
1
0
0
=
1
…...
odd number of “0s”
0
0
=
1
0
0
=
1
…...
even number of “0s”
1 (even number of “0s”)
A1 A2 An=
0 (odd number of “0s”)

## Slide 44: Positive Logic and Negative Logic
If we use the high-voltage to represent the binary number “1”, and we use the low-voltage to represent the binary number “0”, the logic gate in the circuit is working in positive logic.
If we use the high-voltage to represent the binary number “0”, and we use the low-voltage to represent the binary number “1”, the logic gate in the circuit is working in negative logic.

## Slide 45
AND Gate in Positive Logic
F=AB
A
B
F
A
B
F
Because their voltage tables are the same！
OR Gate in Negative Logic
F=A+B
The “AND” gate in positive logic is equal to the “OR” gate in negative logic.

## Slide 46
0V 0V 0V 0 0 0 1 1 1
0V +3.6V 0V 0 1 0 1 0 1
+3.6V 0V 0V 1 0 0 0 1 1
+3.6V +3.6V +3.6V 1 1 1 0 0 0
Voltage Table
Input Output Truth Table Truth Table
VA VB VF A B F A B F
F=AB
F=A+B
Negative
Logic
Positive
Logic

## Slide 47
Positive Logic Negative Logic
Write the dual function of XOR. It is XNOR.
Dual functions of positive logic and negative logic

## Slide 48: 2.3.1 Standard Forms of Logic Functions
1. Standard AND-OR Function
2. Standard OR-AND Function
e.g.
e.g.
2.3 Function Transformation
Notes: Standard AND-OR function: First do the multiplication. Second, do the addition.
Standard OR-AND function: First do the addition. Second, do the multiplication.

## Slide 49: 2.3.2 Canonical Forms of Logic Functions
e.g.
e.g.
Sum of Minterms
1. Canonical AND-OR Function
Also, Sum of Products,
2. Canonical OR-AND Function
Also, Product of Sums,
Product of Maxterms
Notes: Canonical AND-OR Function: is composed of minterms
Canonical OR-AND Function: is composed of maxterms
These product terms are minterms.
These sum terms are maxterms.

## Slide 50
3. Minterm
010
In each product term, each input variable occurs only once.
The input variable is in the original form (A) or the inverted form (A NOT).
The product term is named as Minterm.
If a function is composed of Minterms, it is named as the canonical AND-OR function.
Notes: We use lowercase m to represent minterm.

## Slide 51
Treat A as 1.
Treat A as 0.

## Slide 52
* Properties of Minterm
(1) With n inputs, there are 2n minterms in total.
(2) With any input, only one minterm is “1”.
A,B,C=1,0,1,
(3)

## Slide 53
(4)
(6)
This minterm with “n” input variables has inverting variables with the other “n” minterms.
(5)
The addition of two minterms offsets the inverting variables.

## Slide 54: Exercise
Write the sum of minterms in decimal number.

## Slide 55
000
4. Maxterm
In each sum term, each input variable occurs only once.
The input variable is in the original form (A) or the inverted form (A NOT).
The sum term is named as Maxterm.
If a function is composed of Maxterms, it is named as the canonical OR-AND function.
Notes: We use uppercase M to represent maxterm.

## Slide 56
Treat A as 0.
Treat A as 1.

## Slide 57: Exercise
Write the product of maxterms in decimal number.

## Slide 58
(1) With any input, only one maxterm is“0”.
A,B,C＝1,0,1，
(2)
* Properties of Maxterm

## Slide 59
(5)
(4)
The product of two maxterms offsets the inverting variables.
(3)

## Slide 60
1 1 1 m7 M7
0 0 0 m0 M0
A B C
1 1 0 m6 M6
1 0 1 m5 M5
1 0 0 m4 M4
0 1 1 m3 M3
0 1 0 m2 M2
0 0 1 m1 M1
Minterm
Maxterm
Numbered
Maxterm
Numbered
Minterm

## Slide 61: 2.3.3 Transformation of Logic Functions
1. Write the sum of Minterms of a function.
Step 2: Apply the following formula to recover the missing variable in product terms.
Step 1: Write the standard AND-OR function
Convert the function to sum of Minterms or product of Maxterms.

## Slide 62
All the Minterms of function F(A,B) with two inputs
Example of Minterms
Minterms
Binary numbers for Minterms
Numbered Minterms

## Slide 63
All the Minterms of function F(A,B,C) with three inputs
Example of Minterms
Minterms
Binary numbers for Minterms
Numbered Minterms

## Slide 64
Apply the following formula to recover the missing variable in product terms.
Example: Write the sum of Minterms of a function.

## Slide 65: Exercise
Write the sum of minterms of the function.

## Slide 66
Example: Convert to sum of Minterms.
(1) Get the standard AND-OR function.
Solution:
(2) Recover missing variables.

## Slide 67
Details on function simplification

## Slide 68
Details on recovering missing variables

## Slide 69: Exercise
Write the sum of minterms of the function.

## Slide 70
Step 2: Apply the following formula to recover the missing variable in sum terms.
Step 1: Write the standard OR-AND function
2. Write the product of Maxterms of a function.

## Slide 71
All the Maxterms of function F(A, B) with two inputs
Example of Maxterms
Maxterms
Binary numbers for Maxterms
Numbered Maxterms

## Slide 72
All the Maxterms of function F(A, B, C) with three inputs
Example of Maxterms
Maxterms
Binary numbers for Maxterms
Numbered Maxterms

## Slide 73
Apply the following formula to recover the missing variable in sum terms.
Example: Write the product of Maxterms of a function.

## Slide 74: Exercise
Write the product of maxterms of the function.

## Slide 75
Solution:
Example: Convert to product of Maxterms.
(1) Get the standard OR-AND function.
A+BC=(A+B)·(A+C)
distributive law of addition

## Slide 76
1
A+BC=(A+B)·(A+C)
distributive law of addition

## Slide 77
(2) Recover missing variables.
111
110
011
Apply the following formula

## Slide 78: Exercise
Write the product of maxterms of the function.

## Slide 79
A B C F
1 0 0 1
1 0 1 1
0 1 0 1
1 1 0 1
0 0 0 0
0 0 1 0
0 1 1 0
1 1 1 0
Example: Convert to sum of Minterms by truth table.
2. Function Transformation by Truth Table

## Slide 80
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 0
Write sum of Minterms from Truth Table.
m2
m4
m5
m6

## Slide 81: Exercise
Write the sum of minterms by truth table.

## Slide 82
Example: Convert the following function to product of maxterms by truth table.
A B C F
0 0 0 0
0 0 1 0
0 1 1 0
0 1 0 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 0

## Slide 83
A B C F
0 0 0 0
0 0 1 0
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 0
M0
M1
M3
M7
Write product of Maxterms from Truth Table.

## Slide 84: Exercise
Write the product of maxterms by truth table.

## Slide 85: 2.4.1 Simplification by Formulas
What is the simplest AND-OR function?
2.4 Function Simplification
(1) The number of product terms is the fewest.
(2) The number of variables in each term is the fewest.

## Slide 86
1. Simplification of AND-OR Functions
(1) Apply
Example 1：
Example 2：
(3) Apply
Example 3：
(2) Apply

## Slide 87: Exercise
Simplify the functions.

## Slide 88
(4) Apply the formula
Example 4：
Apply the formula
Notes: We use auxiliary term to help simplification.

## Slide 89: Exercise
Simplify the function.

## Slide 90
Example 5：
Example 6：

## Slide 91: Exercise
Simplify the functions.

## Slide 92
Example 7：
Notes: In order to get the dual function, exchange dot and plus.

## Slide 93: Exercise
Simplify the function.

## Slide 94
Get the dual form
2. Simplification of OR-AND Functions
Example 1：
Get the dual form again
Notes: In order to get the dual function, exchange dot and plus.

## Slide 95
Example 2：
Get the dual form
Get the dual form again

## Slide 96: Exercise
Simplify the function.

## Slide 97: 2.4.2 Simplification by K-Map
K-map is based on the Gray Code in Chapter One.
We can use K-map to simplify the logic functions.
If we draw K-circles on “1” blocks, we get the simplest AND-OR function.
If we draw K-circles on “0” blocks, we get the simplest OR-AND function.

## Slide 98
Rules for K-circles on “1” blocks
(1) We draw a K-circle on 2n (n=0,1,2,…) adjacent “1” blocks.
(2) Each “1” block can be circled many times.
(3) Each K-circle must contain at least one independent “1” block.
(4) 2n adjacent “1” blocks must form a rectangle or a square.

## Slide 99
(9) We can obtain the simplest AND-OR function.
(5) We draw as bigger K-circles as possible.
(7) We can draw a K-circle on the both ends of the K-map.
(6) The fewer K-circles are the better.
(8) For a K-circle, we write “0” as inverted variable (i.e., A NOT) and write “1” as original variable (i.e., A). We get the simplified product term.

## Slide 100: Simplify Logic Function by K-Map Example 1

## Slide 101: K-Map for Function with 2 Input Variables

## Slide 102
F
A
B
0
0
1
m0
m1
m2
m3
1
A is the higher bit Variable. Put A in the vertical direction.
B is the lower bit Variable. Put B in the horizontal direction.
The gray code for variable A is 0 and 1.
The gray code for variable B is 0 and 1.

## Slide 103
F
A
B
0
0
1
m0
m1
m2
m3
1
Function F has 2 input variables.
There are 4 Minterms for function F
00(m0), 01(m1), 10(m2), 11(m3).

## Slide 104
F
A
BC
0
1
10
11
01
m0
m1
m2
m3
m4
m5
m6
m7
00
A is the highest bit variable. Put A in the vertical direction.
BC are the lower bit variables. Put BC in the horizontal direction.
The gray code for variable A is 0 and 1.
The gray code for variables BC is 00, 01, 11, 10.

## Slide 105
F
A
BC
0
1
10
11
01
m0
m1
m2
m3
m4
m5
m6
m7
00
Function F has 3 input variables.
There are 8 Minterms for function F
000(m0), …, 111(m7).

## Slide 106
Find all the Minterms.
Write the simplest AND-OR function by K-Map.
Notes: Add C plus C NOT to recover variable C.
Add B plus B NOT to recover variable B.
Remove parentheses. Write the redundant terms once.
Then, we get all the minterms. Write the numbered minterms.

## Slide 107
00
01
10
11
0
1
BC
A
F
1
1
1
1
F=AC+BC+AB
Put the Minterms in K-map.
Notes: Put the minterms in the K-map.
011 for m3.
Draw K-circles. For the circle on the left, we write A C.
Finally, we get the simplified function.

## Slide 108: Exercise
Simplify the function by K-map.

## Slide 109: Simplify Logic Function by K-Map Example 2

## Slide 110
AB
CD
F
00
01
00
01
10
10
11
11
m0
m1
m2
m3
m4
m5
m6
m7
m8
m9
m10
m11
m12
m13
m14
m15
K-map for the function F

## Slide 111
Function F has 4 input variables.
There are 16 Minterms for function F
0000(m0), …, 1111(m15).
The gray code for variables AB is 00, 01, 11, 10.
The gray code for variables CD is 00, 01, 11, 10.
AB are higher bit variables. Put AB in the vertical direction.
CD are lower bit variables. Put CD in the horizontal direction.

## Slide 112
AB
CD
00
00
01
01
11
11
10
10
1
1
1
1
1
1
1
1
1
F
Recover the product terms in the K-map.
e.g.
0100
1100
1100
1101
1010
1011
0111
0101
1111
1101
0011
0111
1011
1111
Notes: B C NOT D NOT, means if B is 1, C is 0, D is 0, A is 0 or 1, then F is 1.
Mark the block 0100 as 1.
Similarly, we can recover all the product terms.
Draw K-circle. For the left circle, we B C NOT.
Finally, we get the simplified function.

## Slide 113: Exercise
Simplify the function by K-map.

## Slide 114
Rules for K-circle on “0” blocks
(1) We draw a K-circle on 2n (n=0,1,2,…) adjacent “0” blocks.
(2) Each “0” block can be circled many times.
(3) Each K-circle must contain at least one independent “0” block.
(4) 2n adjacent “0” blocks must form a rectangle or a square.

## Slide 115
(9) We can obtain the simplest OR-AND function.
(5) We draw as bigger K-circles as possible.
(7) We can draw a K-circle on the both ends of the K-map.
(6) The fewer K-circles are the better.
(8) For a K-circle, we write “0” as original variable (i.e., A) and write “1” as inverted variable (i.e., A NOT). We get the simplified sum term.

## Slide 116: Simplify Logic Function by K-Map Example 3

## Slide 117
AB
CD
F
00
01
00
01
10
10
11
11
M0
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
M11
M12
M13
M14
M15
K-map for the function F

## Slide 118
Function F has 4 input variables.
There are 16 Maxterms for function F
0000(M0), …, 1111(M15).
The gray code for variables AB is 00, 01, 11, 10.
The gray code for variables CD is 00, 01, 11, 10.
AB are higher bit variables. Put AB in the vertical direction.
CD are lower bit variables. Put CD in the horizontal direction.

## Slide 119
Write the simplest OR-AND function by K-Map.
Example: F(A,B,C,D)=∏M(3,7,11,12,13,14,15)
Can you write all the minterms for the function?
F(A,B,C,D)=∑m(0,1,2,4,5,6,8,9,10)
Numbers from 0 to 15 which are not in maxterms belongs to minterms.
Notes: The function is composed of maxterms.
Can you write all the minterms for the function?
Numbers from 0 to 15 which are not in maxterms belongs to minterms.

## Slide 120
AB
CD
00
00
01
01
11
11
10
10
F
0
0
0
0
0
0
0
F(A,B,C,D)=∏M(3,7,11,12,13,14,15)
Mark the blocks as 0 according to maxterms.
Notes: How to write the K-map?
Method one: mark the blocks as 1 according to minterms. Method two: mark the blocks as 0 according to maxterms.
Draw circles on‘0’blocks. Write the sum terms.
For the horizontal circle, we write A NOT plus B NOT. For the vertical circle, we write C NOT plus D NOT.
Use AND to connect the sum terms. Finally, we get the simplified OR-AND function.

## Slide 121
AB
CD
00
00
01
01
11
11
10
10
F
0
0
0
0
0
0
0
Draw K-circles on‘0’blocks.
Write the sum terms.
Use AND to connect the sum terms.
Notes: How to write the K-map?
Method one: mark the blocks as 1 according to minterms. Method two: mark the blocks as 0 according to maxterms.
Draw circles on‘0’blocks. Write the sum terms.
For the horizontal circle, we write A NOT plus B NOT. For the vertical circle, we write C NOT plus D NOT.
Use AND to connect the sum terms. Finally, we get the simplified OR-AND function.

## Slide 122: Exercise
Simplify the function by K-map.
F(A,B,C,D)=∏M(3,7,11,12,13,14,15)

## Slide 123
In the K-map, drawing circles on “1” blocks will generate the simplest AND-OR function.
In the K-map, drawing circles on “0” blocks will generate the simplest OR-AND function.
Summary

## Slide 124: More Examples on K-map The K-map is given. Draw the K-Circles.

## Slide 125: Draw K-circles on “1” blocks to get the simplest AND-OR function.

## Slide 126
0
0
1
1
A
B
F1
1
1
1
0
0
1
1
A
B
F2
1
1

## Slide 127: The simplest function may not be unique.

## Slide 128
00
01
10
11
0
1
BC
A
F3
1
1
1
1
1
1
Solution 1:

## Slide 129
00
01
10
11
0
1
BC
A
F3
1
1
1
1
1
1
Solution 2:

## Slide 130
00
01
10
11
0
1
BC
A
F4
1
1
1
1
1

## Slide 131
00
01
10
11
0
1
BC
A
F5
1
1
1
1

## Slide 132
00
01
10
11
0
1
BC
A
F6
1
1
1
1
1
1

## Slide 133
00
01
10
11
0
1
BC
A
F7
1
1
1
1
1
1
1
1
F7=1

## Slide 134
AB
CD
F8
00
01
00
01
10
10
11
11
1
1
1
1
1
1
1
1

## Slide 135
AB
CD
00
01
00
01
10
10
11
11
1
1
1
1
1
1
1
1
F9

## Slide 136
AB
CD
00
01
00
01
10
10
11
11
1
1
1
1
1
1
1
1
F10

## Slide 137
AB
CD
00
01
00
01
10
10
11
11
1
1
1
1
1
1
1
1
F11
1
1

## Slide 138
AB
CD
00
01
00
01
10
10
11
11
1
1
1
1
1
1
F12
1
1

## Slide 139: Draw K-circles on “0” blocks to get the simplest OR-AND function.

## Slide 140
AB
CD
F13
00
01
00
01
10
10
11
11
0
0
0
0
0
0
0
0

## Slide 141
AB
CD
00
01
00
01
10
10
11
11
F14
0
0
0
0
0
0
0
0

## Slide 142
AB
CD
00
01
00
01
10
10
11
11
F15
0
0
0
0
0
0