## Slide 1: Chapter 3 Digital Circuit
3.1 CMOS Transistor
3.2 CMOS Gate
3.3 Electrical Characteristics

## Slide 2: 3.1 CMOS Transistor
1 (High-state)
0 (Low-state)
5.0V
3.5V
1.5V
0.0V
Logic Level of 5V

## Slide 3
Gate = “0”
NMOS transistor is OFF.
Gate = “1” (high-state)
NMOS transistor is ON.
drain
source
gate
+
Vgs
NMOS Transistor

## Slide 4
Gate = “1”
PMOS transistor is OFF.
Gate = “0” (low-state)
PMOS transistor is ON.
PMOS Transistor
source
drain
gate
+
Vgs

## Slide 5: 3.2 CMOS Gate
CMOS Inverter
COMS NAND Gate
COMS NOR Gate
CMOS AND-OR-Inverter
CMOS Buffer
Three-State Buffer
Transmission Gate
Schmitt-Trigger Inverter
Open-Drain Output Circuit
Wired Logic

## Slide 6
1. VIN = 0.0V
  Tn is OFF
  Tp is ON
  VOUT  VDD = 5.0V
2. VIN = VDD = 5.0V
  Tn is ON
  Tp is OFF
  VOUT  0V
VDD = +5.0V
VOUT
VIN
Tp
Tn
G
D
S
S
pmos
nmos
CMOS Inverter
VOUT = VIN

## Slide 7
VDD = +5.0V
Vout
Vin
Tp
Tn
VDD
A
Z
Vin | Vout
Low | High
High | Low
CMOS Inverter

## Slide 8
  1. A or B is low-state
  T1 or T3 is OFF
  T2 or T4 is ON
  Z  VDD
  2. A and B are high-state
  T1 and T3 are ON
  T2 and T4 are OFF
  Z  0V
VDD = +5.0V
Z
A
B
T1
T2
T4
T3
Z = A·B
CMOS NAND Gate

## Slide 9
1. A and B are low-state
T1 and T3 are OFF
T2 and T4 are ON
Z  VDD
2. A or B is high-state
T1 or T3 is ON
T2 or T4 is OFF
Z  0V
VDD = +5.0V
Z
A
B
T1
T2
T4
T3
Z = A+B
CMOS NOR Gate

## Slide 10
VDD = +5.0V
A
B
Z
C
D
Z = A·B + C·D
A
B
C
D
z
Q1
Q2
Q3
Q4
Q6
Q5
Q7
Q8
(1) Q1 and Q3 are ON,
or
(2) Q5 and Q7 are ON,
Z is 0V.
Otherwise, Z is high-state.
CMOS AND-OR-Inverter

## Slide 11
VDD = +5.0V
A
Z
CMOS Buffer

## Slide 12: Three-state Buffer
EN=0,
C=1, Tp is OFF
B=1, D=0, Tn is OFF
OUT is floating state
high-impedance disconnected state
EN=1,
C=A , B=0 , D=A
OUT=A
OUT is low-state or high-state
VCC
OUT
EN
A
B
C
D
Tp
Tn
A
EN
OUT

## Slide 13: Transmission Gate
EN = 0，EN_L = 1，
Gate is OFF，
A and B are disconnected
EN = 1，EN_L = 0，
Gate is ON，
bidirectional transmission
A=B
EN
EN_L
A
B

## Slide 14: Schmitt-Trigger Inverter
VOUT
VIN
5.0
2.1
2.9
5.0
VT+
VT-
Input rises to 2.9V, output becomes low-state.
Input falls to 2.1V, output becomes high-state.
input
threshold
VT+
VT-
Hysteresis 2.9V-2.1V=0.8V
2.1V
2.9V

## Slide 15: Open-Drain Output Circuit
A
B
Z
VCC
VCC
’
A
B
Z
NAND Gate
The drain terminal is not connected to the voltage directly.

## Slide 16: Wired Logic
A
B
Z
VCC
VCC
R
C
D
VCC
Z1
Z2
Wired
logic
Z = Z1 · Z2
= A·B · C·D
= A·B · C·D
= A·B + C·D

## Slide 17: Unused inputs of CMOS circuit
X
Z
1k
+5V
X
Z
X
Z

## Slide 18
(1) Logic Level
(2) Fanin
(3) Fanout
(4) Direct Current Noise Margin
(5) Transition Time
(6) Propagation Delay
(7) Diode
(8) Bipolar junction transistor
3.3 Electrical Characteristics

## Slide 19
High State
Low State
VCC
70%VCC
30%VCC
0
VOLmax:Ground+0.1V
VILmax:
VIHmin:
VOHmin:Vcc-0.1V
Logic Level

## Slide 20: Fanin
For a logic gate, the number of inputs allowed is named as “fanin”.
NOR gate ≤4
NAND gate ≤6

## Slide 21: Fanout
“Fanout” is the number of gates that a logic gate can drive.

## Slide 22
74HCT drives 74LS
High-state fanout：
Overall fanout：min(200,10)=10
CMOS: 74HCT
IOH = 4 mA
IOL = 4 mA
IIH = 1 A
IIL = 1 A
TTL: 74LS
IOH = 0.4mA
IOL = 8 mA
IIH = 0.02mA
IIL = 0.4 mA
Low-state fanout：
Fanout

## Slide 23
Residual driving capacity：
CMOS: 74HCT
IOH = 4 mA
IOL = 4 mA
IIH = 1 A
IIL = 1 A
TTL: 74LS
IOH = 0.4mA
IOL = 8 mA
IIH = 0.02mA
IIL = 0.4 mA
74HCT drives 74LS
Fanout

## Slide 24
When two logic gates are cascaded, we use the “direct current noise margin” to measure the noise voltage gap between the driving gate and the driven gate.
If the DC noise margin is positive, the voltage level of both the driving gate and the driven gate are compatible.
Otherwise, the voltage level of the driving gate is destroyed and unrecognizable for the driven gate.
Direct Current Noise Margin

## Slide 25
VOLmax
0.5
VOHmin
2.7
VIHmin
2.0
VILmax
0.8
TTL
VOLmax
0.33
VILmax
0.8
VIHmin
2.0
VOHmin
3.84
CMOS
  Low state: VILmax-VOLmax
  High state: VOHmin-VIHmin
Direct Current Noise Margin

## Slide 26
74HCT drives 74LS
High state: 3.84 – 2.0 = 1.84V
Low state: 0.8 – 0.33 = 0.47V
VOLmax
0.33
VILmax
0.8
VIHmin
2.0
VOHmin
3.84
74HCT
VOLmax
0.5
VOHmin
2.7
VIHmin
2.0
VILmax
0.8
74LS
74LS drives 74HCT
High state: 2.7 – 2.0 = 0.7V
Low state: 0.8 – 0.5 = 0.3V
Therefore, they are compatible.

## Slide 27
10%
10%
rise time tr
Fall time tf
In the digital circuit, the time required for the circuit output to change between the low-state and high-state voltage is named as the “transition time”.
Transition Time
circuit output from low-state to high-state
circuit output from high-state to low-state

## Slide 28
VIN
VOUT
When the voltage level of the circuit input changes, and the voltage level of the circuit output changes correspondingly, the total time required is named as the “propagation delay”.
Propagation Delay
The input changes to be high, and the output changes to be low
The input changes to be low, and the output changes to be high

## Slide 29
＋
Diode
Anode
Cathode
+
Rf
Vd
forward-biased
voltage level of anode is higher than that of cathode
+
reverse-biased
voltage level of anode is lower than that of cathode

## Slide 30
A
B
D1
D2
R
VCC 5V
Y
Input (5V, 5V), output ≈ 5V
Input (0V, 5V), output = 0.6V
diode-drop 0.6V
Diode

## Slide 31: Bipolar junction transistor
base
collector
emitter
VCC
vo
+
-
vi
+
-
RB
RC
iC
NPN Transistor
NPN Transistor Inverter
if the voltage level of “base” is high, the NPN transistor is conductive.
Otherwise, the NPN transistor is not conductive.

## Slide 32
3.4 Calculation of current, voltage, and resistance
Kirchhoff’s Current Law（KCL）：Total current entering a junction is equal to total current leaving it.
（1） Calculation of current
Notes: Ampere /ˈæmpeə/
Ohm /oʊm/
Volt /voʊlt/
Kirchhoff /ˈkɜrkhɔf/

## Slide 33
Example：I1=-2A，I2=6A，I3=3A，I5=-3A.
What are the currents I4 and I6 ?
Solution：

## Slide 34
（2） Calculation of voltage
Kirchhoff's Voltage Law（KVL）：Algebraic sum of voltages around a loop equals to zero.

## Slide 35
Example：What are the current I and the voltage U ?
Solution：
Based on point a

## Slide 36
（3） Calculation of potential
Potential：Uab=Va-Vb
Voltage is the difference of potentials.

## Slide 37
Example：Based on a and b, what are the potentials of a, b, c, d ?
Based on point a
Solution：

## Slide 38
Based on point b：

## Slide 39
（4）Calculation of resistance
Resistors in series
Equivalent resistance：
Shared voltage：

## Slide 40
Shared voltages of two resistors：

## Slide 41
Parallel resistors
Conductance（Reciprocal of resistance）：

## Slide 42
Equivalent resistance of two resistors in parallel：
Shared current：
Shared currents of two resistors in series：

## Slide 43
Example：What is the equivalent resistance Rab ?
Solution：5Ω and 20Ω are in parallel.
It is in series with 3Ω and 5Ω defined as R´.

## Slide 44
The 12Ω is in parallel with 4Ω.
It is in series with 1Ω.

## Slide 45
Example：What is the current Ix ?
Solution：

## Slide 46
I is shared with I1 and I2 .
I1 is shared with R4 (Ix) and R5 .

## Slide 47
Superposition theorem
The strategy used in the superposition theorem is to eliminate all but one source of power within a network at a time. Then, we use series and parallel circuit analysis techniques to determine voltage drops and currents within the modified network for each power source separately.
This process is then repeated sequentially by individually evaluating the circuit for every voltage and current source in the system. After each individual analysis has been completed, the voltage and current values are all “superimposed” on top of each other (added algebraically) to find the actual voltage drops and currents with all sources active.

## Slide 48
（5）Thevenin's theorem
The ideal model is in series, we calculate the open circuit voltage Uoc，and the equivalent resistance Req .
N：A resistor network that provides energy

## Slide 49
Example：Based on Thevenin's theorem，what is the voltage U of the 6Ω resistor ?
Solution：Disconnect 6Ω. Define the open circuit voltage UOC .
Open circuit voltage：
Current source

## Slide 50
Voltage source (1V) is short circuited.
Current source (2A) is open circuited.
Equivalent resistance：
Voltage U of 6Ω：
（d）Thevenin's Model

## Slide 51
1.5V
0.75V
3.5V
0.25V
0.25A
0.25A
2A
2A
1.75A
0.25A

## Slide 52
（6）Norton's theorem
The ideal model is in parallel, we calculate the short circuit current isc，and the equivalent resistance Req .

## Slide 53
Example：Given iC=0.75i1, what are the Thevenin's model and Norton's model ?
Transistor
Controlled Current Source

## Slide 54
Open circuit voltage：
Given

## Slide 55
Given iC=0.75i1
Short circuit current：

## Slide 56
(c)Thevenin's model
Equivalent resistance：
(d)Norton's model

## Slide 57
（7）Maximum power transfer theorem
How to obtain maximum power from a circuit for a resistance load ?
Load power：
Req and RL share the voltage.

## Slide 58
To get the maximum power P，derivation of load resistance：
The condition for the maximum power of load resistance：
Maximum power of resistance load：

## Slide 59
Example：Calculate（1）the resistance of RL for the maximum power,（2）the maximum power,（3）the power transmission efficiency of voltage source 10V.
Calculate the equivalent resistance，and get Thevenin's model（b）.

## Slide 60
Given ，the maximum power：
Two resistors in series for open circuit voltage：
Two resistors in parallel for Equivalent resistance：
Disconnect the load RL .

## Slide 61
To calculate equivalent resistance:
（Previous example）
Equivalent resistance：
Two resistors in parallel for Equivalent resistance：
Voltage source (1V) is short circuited.
Current source (2A) is open circuited.

## Slide 62
Load current：
Load voltage：
Driven current i：

## Slide 63
Transmission power：
Power of voltage source 10V：

## Slide 64
（8）Why are most power sources the alternating current ？
The alternating current generator has a simple structure, low cost, and high efficiency.
The direct current generator has a more complex structure, high cost, and low efficiency.
The alternating current power can easily increase and decrease the voltage through a transformer.
The direct current voltage boosting is relatively complex, costly, immature in technology, and inefficient.

## Slide 65
（9）How to convert alternating current into direct current ？
Waveform of alternating current
Only positive cycles can pass
Negative cycles are blocked
Cycles are cut off in half

## Slide 66
half-wave rectification
We only get half waves
Use four diodes to get all waves
Rectifier

## Slide 67
Current of positive cycles
Current of negative cycles
Half waves
All waves

## Slide 68
Full-wave rectifier
All waves
Add the capacitor
Close to direct current