## Slide 1: Chapter 4 Combinational Logic Circuit
4.1 Analysis of Combinational Logic Circuit
4.2 Design of Combinational Logic Circuit
4.3 Representative Combinational Logic Circuits
4.4 Hazard of Combinational Logic Circuit

## Slide 2: Classification of Logic Circuits
Logic circuits are divided into two classes.
1. Combinational Logic Circuit:
A combinational circuit uses logic gates only, not related to time.
(i.e., AND gate, OR gate, NOT gate)
2. Sequential Logic Circuit:
A sequential circuit uses flip-flops and logic gates, related to time.

## Slide 3: 4.1 Analysis of Combinational Circuit
Write Truth Table
Circuit
Diagram
Write Logic
Function
Simplification
by Formulas
Describe
Role of the
Circuit
Steps for Combinational Circuit Analysis
(Read the given
circuit diagram)
Notes: Read the circuit diagram. Write the logic function. Simplify the function. Describe the role of the circuit.
Sometimes, we need the truth table to describe the role of the circuit.

## Slide 4
A
B
F
AB ( common term )
AAB
BAB
Example 1: Analyze the Following Circuit
NAND

## Slide 5
Calculate the multiplication.
Write XOR by definition.
Apply De Morgan’s Law.

## Slide 6
A=A1A0 , B=B1B0 are two-bit Binary numbers.
F
A1
B1
A0
B0
Example 2: Analyze the Following Circuit
Inverter
XOR
NAND

## Slide 8
F= A1 B1 A0 B0= (A1 B1)(A0 B0)
If A1= B1 ; A0= B0 Then F=1
Then F=0
If A1≠B1 ; A0≠ B0
A1= B1 ; A0≠ B0
A1≠ B1 ; A0= B0
This is a circuit to compare two 2-bit binary numbers.
(Numerical Comparator)

## Slide 9
F
C
C
B
B
A
A
Example 3: Analyze the Following Circuit
NAND
AND
NOR
common term
Extract the common term.
Apply De Morgan’s law.

## Slide 10
A B C F
0 0 0 1
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 1
If the inputs are identical, then output F=1. Otherwise, output F=0. It is a “unanimous circuit”.
Write the truth table of the function.

## Slide 11: Exercise

## Slide 12
A
B
F
1: Analyze the Following Circuit
Write the logic function, simplify the function by formulas, write the truth table (optional), describe the role of the circuit.

## Slide 13
A=A1A0 , B=B1B0 are two-bit Binary numbers.
F
A1
B1
A0
B0
2: Analyze the Following Circuit
Write the logic function, simplify the function by formulas, write the truth table (optional), describe the role of the circuit.

## Slide 14
F
C
C
B
B
A
A
3: Analyze the Following Circuit
Write the logic function, simplify the function by formulas, write the truth table (optional), describe the role of the circuit.

## Slide 15: 4.2 Design of Combinational Circuit
1. Steps to design a combinational circuit
(1) Define input variable and output variable.
(2) Define states for “0” and “1”.
(3) Write the truth table.
(4) Simplify the function.
(5) Draw the circuit diagram.

## Slide 16
Example 1: We have three inputs. We count the total number of ones in the inputs. If the total number is odd, the output is 1. Otherwise, the output is 0. Design the circuit.
(1) Define variables and states
Inputs : A, B, C
Output : F
F=1: the total number is odd.
F=0: the total number is even.

## Slide 17
F
A
BC
00
01
11
10
0
1
0
0
0
0
1
1
1
1
A B C F
0 0 0 0
0 0 1 1
0 1 0 1
0 1 1 0
1 0 0 1
1 0 1 0
1 1 0 0
1 1 1 1
（2）Truth Table
（3）Simplification

## Slide 18
（4）Function Transformation
（5）Circuit Diagram
C
B
A
F
Fewer logic gates!
XOR gate

## Slide 19
Extract common term.
Write XOR, XNOR by definition.
Inverted XOR equals XNOR.
Write XOR by definition.

## Slide 20
Example 2: Design a circuit to detect 8421BCD code. If the input satisfies the condition 3≤X≤6, then output F=1. Otherwise, output F=0. Implement the circuit by “NAND” gates only.
(1) Define variables and states
Inputs : A, B, C, D
Output : F
F=1: means the input satisfies condition 3≤X≤6.
F=0: means the other cases.
Notes: The input satisfies the inequality. X is no less than 3 and no greater than 6.

## Slide 21
A B C D F
0 0 0 0 0
0 0 0 1 0
0 0 1 0 0
0 0 1 1 1
0 1 0 0 1
0 1 0 1 1
0 1 1 0 1
0 1 1 1 0
1 0 0 0 0
1 0 0 1 0
1 0 1 0 d
1 0 1 1 d
1 1 0 0 d
1 1 0 1 d
1 1 1 0 d
1 1 1 1 d
A B C D F
（2）Truth Table
3≤X≤6

## Slide 22
The output d is the “don’t care term”.
The value of d can be 0 or 1.
1010, …, 1111 are invalid inputs for the 8421 BCD code.
So we use the “don’t care term” d to represent those outputs.

## Slide 23
F
AB
CD
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
0
0
0
0
0
1
1
1
1
（3）Function Simplification

## Slide 24
F
B
C
D
B
C
B
D
（4）Circuit Diagram
We are required to implement the circuit by NAND gates only!

## Slide 25
Hint: Change OR Gate into NAND Gate

## Slide 26
Example 3: Design the combinational circuit by NOR gates only. If a 4-bit binary number is an integer multiple of 5, then output F=1. Otherwise, output F=0.
(1) Define variables
We use B4B3B2B1 to define the 4-bit binary number.

## Slide 27
1 0 1 0 1
1 1 1 1 1
0 0 0 0 1
0 1 0 1 1
0 0 0 1 0
0 1 1 0 0
B4 B3 B2 B1 F
B4 B3 B2 B1 F
1 0 0 0 0
1 0 0 1 0
0 0 1 0 0
1 0 1 1 0
0 0 1 1 0
1 1 0 0 0
0 1 0 0 0
1 1 0 1 0
1 1 1 0 0
0 1 1 1 0
（2）Truth Table
Integer multiple of 5: 0,5,10,15

## Slide 28
F
B4B3
B2B1
00
00
01
01
11
11
10
10
0
0
1
0
1
0
0
0
0
0
0
0
0
1
0
1
（3） Function Simplification
We are required to implement the circuit by NOR gates only!
Draw K-circles on “0” blocks.
Notes: For the bottom left K-circle, B4 equals 1, B2 equals 0.
So we write B4 NOT plus B2.
Similarly, you can write all the sum terms for the other K-circles.
Finally, change the OR gate into the NOR gate.

## Slide 29
For the bottom left K-circle, B4 equals 1, B2 equals 0.
So we write B4 NOT plus B2.
Similarly, you can write all the sum terms for the other K-circles.
Finally, change the AND gate into the NOR gate.
Notes

## Slide 30
Hint: Change AND Gate into NOR Gate
Notes: Put an inverter on A, and put an inverter on B.
Get a NOR gate for them.

## Slide 31
Put an inverter on top of A, and put an inverter on top of B.
Get a NOR gate for them.
Notes

## Slide 32
F
（5）Circuit Diagram
NOR gate

## Slide 33: Exercise

## Slide 34
1: There are three inputs. Count the total number of ones in the inputs. If the total number is odd, the output is 1. Otherwise, the output is 0. Design the logic circuit.
2: Design a circuit to detect 8421BCD code. If the input satisfies the condition 3≤X≤6, then output F=1. Otherwise, output F=0. Implement the circuit by “NAND” gates only.
3: Design the combinational circuit by NOR gates only. If the input 4-bit binary number is an integer multiple of 5, then output F=1. Otherwise, output F=0.

## Slide 35
How to prove it?
NAND gate and NOR gate are universal logic gates. That is to say, each of them can implement any logic gate circuit.
Any logic function can be composed of AND, OR, NOT gate.
Prove: the “NAND” gate can implement the AND gate, the OR gate, and the NOT gate.

## Slide 36
（1）
A
A
Prove the generality of NAND gate.
Use NAND gate to implement NOT Gate
Inverter

## Slide 37
（2）
A
B
AB
Use NAND gate to implement AND Gate
Inverter
NAND

## Slide 38
（3）
A+B
A
A
B
B
Use NAND gate to implement OR Gate
Prove the universality of NOR gate in a similar way.
Inverter
NAND

## Slide 39: Exercise

## Slide 40
（1）
Prove the generality of NOR gate.
Use NOR gate to implement NOT Gate
Use NOR gate to implement AND Gate
（2）
（3）
Use NOR gate to implement OR Gate

## Slide 41: 4.3 Representative Combinational Circuits
1. Adder and Subtractor
2. Code Converter
3. Numerical Comparator
4. Encoder
5. Decoder
6. Data Selector

## Slide 42: 4.3.1 Adder and Subtractor
1.Half Adder
A B S C
0 0 0 0
0 1 1 0
1 0 1 0
1 1 0 1
S=A B C=AB
A
B
S
C
AND
XOR
0
＋ 1
1
1
A
B
S
C
Notes: In half adder, we will calculate A plus B. A and B are inputs.
S is the sum result, and C is the carry output.
Can you write the logic function of S and C?
So we use XOR gate to implement the sum result, and use AND gate to implement the carry output.

## Slide 43
In half adder, we will calculate A plus B. A and B are inputs.
S is the sum result, and C is the carry output.
Can you write the logic function of S and C?
We use XOR gate to implement the sum result, and use AND gate to implement the carry output.
Notes

## Slide 44
We can implement the calculation circuit in computer based on half adder.
What is the role of half adder?

## Slide 45: Exercise

## Slide 46
1: Write the truth table of the half adder
2: Write the logic functions of the half adder

## Slide 47
Ci
FA
Ai
Bi
Ci-1
Si
2. Full Adder
1 1 1 1 1
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 1 0 1
0 0 1 0
1 1 0 0 1
Ai Bi Ci-1 Si Ci
C: Carry
S: Sum

## Slide 48
1
1
1
1
Ai
BiCi-1
00
01
11
10
0
1
0
0
0
0
Si

## Slide 49
1
1
1
1
Ai
BiCi-1
00
01
11
10
0
1
0
0
0
0
Ci

## Slide 50
Si
Ci
Bi
Ci-1
Ai
Ai
Bi
Ci-1

## Slide 51
3. Integrated Adder
1
2
3
4
5
6
7
8
9
10
11
12
13
14
74183
1Ai
1Bi
1Ci-1
1Ci
1Si
2Ci
2Ci-1
2Bi
2Ai
2Si
Vcc
GND
Chip Pin Diagram
Voltage
Ground

## Slide 52
1
2
3
4
5
6
7
8
9
10
11
12
13
14
74183
1Ai
1Bi
1Ci-1
1Ci
1Si
2Ci
2Ci-1
2Bi
2Ai
2Si
Vcc
GND
Voltage
“0”
Output
Output
A1
A2
B1
B2
Output
Calculate: A2A1 + B2B1
Ground

## Slide 54
The carry look-head adder saves the time of passing around the carry signal.
ＣO
ＣI
Ａ0
B0
S0
C0
ＣO
ＣI
Ａ1
B1
S1
C1
ＣO
ＣI
Ａ2
B2
S2
C2
ＣO
ＣI
Ａ3
B3
S3
C3
∑
∑
∑
∑
4. Carry Look-Ahead Adder

## Slide 55
Carry Look-Ahead Adder
C0= A0 B0+ A0 C0-1+ B0 C0-1= A0 B0+ (A0 +B0)C0-1
C1= A1 B1+ (A1 +B1)C0 = A1 B1+ (A1 +B1)[A0 B0+
(A0 +B0)C0-1]
C2= A2 B2+ (A2 +B2)C1 = A2 B2+ (A2 +B2){A1 B1+
(A1 +B1)[A0 B0+ (A0 +B0)C0-1]}
C3= A3 B3+ (A3 +B3)C2 = A3 B3+ (A3 +B3){A2 B2+
(A2+B2){A1B1+(A1+B1)[A0 B0+ (A0 +B0)C0-1]}}

## Slide 56
1
2
3
4
5
6
7
8
11
12
13
14
15
16
74283
S1
C0-1
C3
Vcc
GND
10
9
B1
A1
S0
A0
B0
B2
A2
S2
A3
B3
S3
A3A2A1A0 + B3B2B1B0
C0-1
C3
S3
S2
S1
S0
Chip pin diagram of Carry Look-Ahead Adder

## Slide 57
Convert 8421 BCD to Excess-Three Code.
74283
S1
B1
A1
S0
A0
B0
B2
A2
S2
A3
B3
S3
C0-1
0
0
1
1
A
B
C
D
8421BCD
W
X
Y
Z
Excess-Three Code

## Slide 58
1 0 1 0 0
1 1 1 1 1
0 0 0 0 0
0 0 1 1 1
0 1 0 1 1
0 1 1 0 1
Gi
FS
Ai
Bi
Gi-1
Di
Ai Bi Gi-1 Di Gi
1 0 0 1 0
1 1 0 0 0
5.Full Subtractor
D：Difference
G: Borrow bit

## Slide 59
1
1
1
1
BiGi-1
00
01
11
10
0
0
0
0
0
1
Ai
Di

## Slide 60
1
1
1
1
BiGi-1
00
01
11
10
0
0
0
0
1
0
Ai
Gi

## Slide 61
Bi
Gi-1
Ai
Ai
Bi
Gi-1
Di
Gi

## Slide 62
Bi
Gi-1
Ai
Ai
Bi
Gi-1
Di
Gi
Bi
Ci-1
Ai
Ai
Bi
Ci-1
Si
Ci
Full Adder
Full Subtractor

## Slide 63: 4.3.2 Code Converter
A B C D W X Y Z
0 0 0 0 0 0 1 1
0 0 0 1 0 1 0 0
0 0 1 0 0 1 0 1
0 0 1 1 0 1 1 0
0 1 0 0 0 1 1 1
0 1 0 1 1 0 0 0
0 1 1 0 1 0 0 1
Example 1: Convert the 8421BCD Code to Excess-Three Code
Input: 8421BCD code
Output: Excess-three code

## Slide 64
0 1 1 1 1 0 1 0
1 0 0 0 1 0 1 1
1 0 0 1 1 1 0 0
1 0 1 0 d d d d
1 0 1 1 d d d d
1 1 0 0 d d d d
1 1 0 1 d d d d
1 1 1 0 d d d d
1 1 1 1 d d d d
A B C D W X Y Z
Invalid inputs
Notes: The 8421 BCD code is the input and represented as ABCD.
The excess-three code is the output and represented as WXYZ.
The excess-three code equals the 8421 BCD code plus 0011.
The 8421 BCD code covers from 0 to 9.
The numbers from 1010 to 1111 are invalid for 8421 BCD code.
Their outputs are denoted as “d” (do not care term), which could be 0 or 1.
Next, we will draw the K-map for each output of the excess-three code, and write their logic expressions.

## Slide 65
The 8421 BCD code is the input and represented as ABCD.
The excess-three code is the output and represented as WXYZ.
The excess-three code equals the 8421 BCD code plus 0011.
The 8421 BCD code covers from 0 to 9.
The numbers from 1010 to 1111 are invalid for 8421 BCD code.
Their outputs are denoted as “d” (do not care term), which could be 0 or 1.
Notes

## Slide 66
Next, we use K-map to simplify the output functions (the four bits of the excess-three code).
The “d ” block helps to expand the K-circle, making bigger K-circles.
K-circles must cover all the “1” blocks, and the necessary “d” blocks.

## Slide 67
W
AB
CD
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
0
0
1
1
0
1
1
1
0
W=A+BD+BC
Notes: The 1st circle covers 4 blocks, including two “1s” and two “ds”.
The 2nd circle is similar.
The 3rd circle covers 8 blocks.

## Slide 68
X
AB
CD
00
00
01
01
11
11
10
10
d
d
d
d
d
d
1
1
1
0
1
1
0
0
0
0
Notes: The 1st circle covers two blocks.
The 2nd circle covers four blocks in the mirror direction.
The 3rd circle is similar.

## Slide 69
Y
AB
CD
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
1
1
1
0
0
1
0
0
1
Notes: The 1st circle covers the whole column.
The 2nd circle is similar.

## Slide 70
Z
AB
CD
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
0
1
1
0
1
0
0
1
1
Notes: The only circle covers two columns.

## Slide 71
Can you draw the circuit diagram for the outputs (the excess-three code)?

## Slide 72
Z
D
W
A
B
D
B
C
X
B
C
D
B
D
B
C
Y
C
D
C
D
W=A+BD+BC
Notes: Can you draw the circuit diagram of the outputs for the excess-three code?
Look at function W. We have B dot D, B dot C. We have three inputs for the OR gate.
Z equals D NOT.

## Slide 73
B4 B3 B2 B1 G4 G3 G2 G1
0 0 0 0 0 0 0 0
0 0 0 1 0 0 0 1
0 0 1 0 0 0 1 1
0 0 1 1 0 0 1 0
0 1 0 0 0 1 1 0
0 1 0 1 0 1 1 1
0 1 1 0 0 1 0 1
Example 2: Convert the Four-Bit Binary Number to Gray Code
Output: gray code
Input: binary number
Notes: B4B3B2B1 denotes the binary code.
G4G3G2G1 denotes the gray code.
The relation of binary code and gray code is defined in Chapter One.
Next, we will draw the K-maps for the outputs of gray code, and write their logic expressions.

## Slide 74
0 1 1 1 0 1 0 0
1 0 0 0 1 1 0 0
1 0 0 1 1 1 0 1
1 0 1 0 1 1 1 1
1 0 1 1 1 1 1 0
1 1 0 0 1 0 1 0
1 1 0 1 1 0 1 1
1 1 1 0 1 0 0 1
1 1 1 1 1 0 0 0
B4 B3 B2 B1 G4 G3 G2 G1
Notes: How to write the 4-bit gray code?
Look at the higher two bits. 00 covers 4 lines, 01 covers 4 lines, 11 covers 4 lines, and 10 covers 4 lines.
Look at the lower tow bits. 00, 01, 11, 10. reflect the gray code in the mirror direction.

## Slide 75
B4B3B2B1 denotes the binary number.
G4G3G2G1 denotes the gray code.
The relation of binary code and gray code is defined in Chapter One.
Next, we will draw the K-maps for the outputs, and write logic functions.
Notes

## Slide 76
Next, we use K-map to simplify the output functions (the four bits of the gray code).

## Slide 77
G4
B4B3
B2B1
00
00
01
01
11
11
10
10
1
1
1
1
1
1
0
0
0
1
1
0
0
0
0
0
G4= B4
Notes: The only circle covers 8 blocks.

## Slide 78
G3
B4B3
B2B1
00
00
01
01
11
11
10
10
0
0
0
0
1
1
0
0
1
1
1
0
1
1
1
0
Notes: The 1st circle covers the whole row.
The 2nd circle is similar.

## Slide 79
G2
B4B3
B2B1
00
00
01
01
11
11
10
10
1
1
0
0
1
1
0
1
1
0
0
1
0
1
0
0
Notes: The 1st circle covers four blocks in the mirror direction.
The 2nd circle covers four blocks.

## Slide 80
G1
B4B3
B2B1
00
00
01
01
11
11
10
10
0
1
0
1
1
0
1
0
0
0
1
1
0
1
1
0
Notes: The 1st circle covers the whole column.
The 2nd circle is similar.

## Slide 81
Can you draw the circuit diagram for the outputs (the gray code)?

## Slide 82
B3
B4
B2
B1
G3
G4
G2
G1
Notes: This is diagram of the code conversion circuit, which converts the binary code into the gray code.
G4 equals B4.
G3 equals the XOR result of B4 and B3.

## Slide 83
This is diagram of the code conversion circuit, which converts the binary number into the gray code.
Notes

## Slide 84: Exercise

## Slide 85
2: Convert the Four-Bit Binary Number to Gray Code
The first half of the truth table.
The second half of the truth table.
1: Convert the 8421BCD Code to Excess-Three Code
Design the circuit.

## Slide 86: 4.3.3 Numerical Comparator
A B F1(A>B) F2(A=B) F3(A<B)
0 0 0 1 0
0 1 0 0 1
1 0 1 0 0
1 1 0 1 0
One-Bit Numerical Comparator
Inputs: binary numbers
Outputs: comparison results
Notes: If A equals B, F2 is 1.
If A is larger than B, F1 is 1.
If A is less than B, F3 is 1.

## Slide 87
If A equals B, F2 is 1.
If A is bigger than B, F1 is 1.
If A is smaller than B, F3 is 1.
Notes

## Slide 88
Can you draw the circuit diagram for the outputs (comparison results)?

## Slide 89
A
B
F1
F2
F3
F1(A>B)
F2(A=B)
F3(A<B)
common term
AND
XOR
Inverter
Notes: This circuit diagram implements the One-Bit Numerical Comparator.
A XOR B is the common term to the outputs F1, F2, and F3.
If A is 1, B is 0, then A is larger that B.
If A and B are the same, then A equals B.
If A is 0, B is 1, then A is less than B.
A XOR B is the common term.
Write the logic functions for F1, F2, F3 according to the circuit diagram.
Simplify the functions to see what we can get.
The circuit diagram implements functions F1, F2, F3.

## Slide 90
This circuit diagram implements the One-Bit Numerical Comparator.
A XOR B is the common term to the outputs F1, F2, and F3.
Notes

## Slide 91: Exercise

## Slide 92
1: Write the truth table of the 1-bit numerical comparator
2: Write the logic functions of the 1-bit numerical comparator

## Slide 93
B=B3 B2 B1 B0
Given: A=A3 A2 A1 A0
Four-Bit Numerical Comparator

## Slide 94
A<B:
A=B:
F2= (A3 B3)(A2 B2)(A1 B1)(A0 B0)
+ (A3 B3)(A2 B2)(A1 B1)A0B0
F3=A3B3+(A3 B3)A2B2+(A3 B3)(A2 B2)A1B1
A>B:
+ (A3 B3)(A2 B2)(A1 B1)A0B0
F1=A3B3+(A3 B3)A2B2+(A3 B3)(A2 B2)A1B1

## Slide 95
1
2
3
4
5
6
7
8
11
12
13
14
15
16
7485
Vcc
GND
10
9
Chip Pin Diagram of
B3
B0
B2
B1
B=B3 B2 B1 B0
A3
A2
A1
A0
A=A3 A2 A1 A0
A<B
A=B
A>B
Comparison input of lower bit：
A>B，A=B，A<B
FA<B
FA>B
FA=B
Comparison result：
FA>B，FA=B，FA<B
Four-Bit Numerical Comparator

## Slide 96
“0”
“1”
“0”
A3
A2
A1
A0
B3
B2
B1
B0
A3
A2
A1
A0
B3
B2
B1
B0
A>B
A=B
A<B
FA>B
FA=B
FA<B
(1)
Lower 4 bits
A7
A6
A5
A4
B7
B6
B5
B4
A3
A2
A1
A0
B3
B2
B1
B0
A>B
A=B
A<B
FA>B
FA=B
FA<B
FA>B
FA=B
FA<B
(2)
Higher 4 bits
Eight-Bit Numerical Comparator

## Slide 97: 4.3.4 Encoder
X1
X2n
Y1
Yn
Encoder
2n－n
I0
I1
I7
Y0
Y1
Y2
8-3
Encoder
Encoder coverts a decimal number to the equivalent binary number.
1. 8-3 Encoder
Notes: For the encoder, we have the nth power of 2 inputs, and n outputs.
Specifically, in the 8 to 3 encoder, we have 8 inputs (decimal values from 0 to 7) and 3 outputs (binary values from 000 to 111).
Inputs from I_0 NOT to I_7 NOT are low-level voltage effective.

## Slide 98
The encoder converts decimal numbers to binary numbers.
Each of the n th power of 2 decimal numbers is converted to a n-bit binary number.
Look at the 8 to 3 encoder.
The inputs are decimal numbers from 0 to 7.
The output is a 3-bit binary number.
The inputs use low-level voltage.
We use inverter to indicate the low-level voltage input.
Notes

## Slide 99
For the encoder, we have the nth power of 2 inputs, and n outputs.
Specifically, in the 8 to 3 encoder, we have 8 inputs (decimal values from 0 to 7) and 3 outputs (binary values from 000 to 111).
Inputs from I_0 NOT to I_7 NOT are low-level voltage effective.
Notes

## Slide 100
Truth Table of 8-3 Encoder
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0
At one time, only one decimal number requires encoding.
Notes: The decimal value 0 (I_0 NOT equals 0), is encoded as the binary value 000 (Y2Y1Y0 equals 000).
The decimal value 7 (I_7 NOT equals 0), is encoded as the binary value 111 (Y2Y1Y0 equals 111).
0 is the encoding signal for each decimal number.

## Slide 101
Constraint of 8-3 Encoder：
Also：

## Slide 102
Let’s look at the Truth Table of 8-3 Encoder.
0 is the encoding signal for each decimal number.
The decimal number 0 is encoded as the binary number 000.
The decimal number 7, is encoded as the binary number 111.
Notes

## Slide 103
The decimal value 0 (I_0 NOT equals 0), is encoded as the binary value 000 (Y2 Y1 Y0 equals 000).
The decimal value 7 (I_7 NOT equals 0), is encoded as the binary value 111 (Y2 Y1 Y0 equals 111).
Notes

## Slide 104
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0
Y2?

## Slide 105
Let：
How to simplify Y2？

## Slide 106
Constraint

## Slide 108
By
：

## Slide 109
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0
Y2?

## Slide 110
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0
Y1?

## Slide 111
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0
Y0?

## Slide 112
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0

## Slide 113: Exercise

## Slide 114
Write the truth table of the 8-3 encoder.

## Slide 115
2. Priority Encoder
When multiple signals (decimal numbers from 0 to 7) request encoding at the same time, which one to choose?
The Priority Encoder (chip serial number: 74LS148) only responds to the signal with the highest priority.

## Slide 116
Y2
Y1
Y0
VCC
YS
YEX
74LS148
ST
I0
I1
I2
I3
I4
I5
I6
I7
1
2
3
4
5
6
7
8
9
10
11
16
15
14
12
13
Priority
= 0
then the chip works.
= 1
If
If
then (outputs are invalid)
Notes: Inputs from I_0 NOT to I_7 NOT are low-level voltage effective.
Outputs from Y_2 NOT to Y_0 NOT are low-level voltage effective.
The decimal value 0 (I_0 NOT equals 0), is encoded as the binary value 111 (Y2Y1Y0 equals 111).
The decimal value 7 (I_7 NOT equals 0), is encoded as the binary value 000 (Y2Y1Y0 equals 000).
The input I_7 NOT has the highest priority. The input I_0 NOT has the lowest priority.
ST_NOT is the enabling pin.
If ST is disabled, all the outputs are blocked to 1.

## Slide 117
The input number I0,…,I7 NOT uses low-voltage.
Decimal number 7 has the highest priority. Decimal number 0 has the lowest priority.
The chip pin ST NOT controls the working status.
If ST NOT is 0, the priority encoder is working.
If ST NOT is 1, the encoding outputs Y2Y1Y0 NOT are 1 (invalid).
The encoding result Y2Y1Y0 NOT uses low-voltage.
Notes

## Slide 118
Inputs from I_0 NOT to I_7 NOT are low-level voltage effective.
Outputs from Y_2 NOT to Y_0 NOT are low- level voltage effective.
The decimal value 0 (I_0 NOT equals 0), is encoded as the binary value 111 (Y2Y1Y0 equals 111).
The decimal value 7 (I_7 NOT equals 0), is encoded as the binary value 000 (Y2Y1Y0 equals 000).
The input I_7 NOT has the highest priority. The input I_0 NOT has the lowest priority.
ST_NOT is the enabling pin.
Notes

## Slide 119
Y2
Y1
Y0
VCC
YS
YEX
74LS148
ST
I0
I1
I2
I3
I4
I5
I6
I7
1
2
3
4
5
6
7
8
9
10
11
16
15
14
12
13
Then, (output) means there is no input signal.
If
and (all inputs are 1)
Notes: If ST is enabled, and all the inputs are 1, then Ys is 0.

## Slide 120
If there is no input signal, the output Ys is 0.
If ST NOT is 0, it means the priority encoder is working.
If inputs from I0 NOT to I7 NOT are 1, it means decimal numbers from 0 to 7 have no encoding request.
Notes

## Slide 121
Y2
Y1
Y0
VCC
YS
74LS148
ST
I0
I1
I2
I3
I4
I5
I6
I7
YEX
1
2
3
4
5
6
7
8
9
10
11
16
15
14
12
13
then (output) means there are input signals.
If
and
any inputs are 0,
Notes: If ST is enabled, and any of the inputs are 0, Yex is 0.

## Slide 122
If there are input signals, the output Yex NOT is 0.
If ST NOT is 0, the priority encoder is working.
If any inputs from I0 NOT to I7 NOT are 0, it means any decimal numbers from 0 to 7 have encoding requests.
Notes

## Slide 123
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
Truth Table of Priority Encoder
Notes: If ST_NOT is 1, the encoder is disabled.
If all the inputs are 1, Ys is 0 (there is no input signal).
If I_7 NOT is 0, the decimal 7 is encoded as 000.
If I_0 NOT is 0, the decimal 0 is encoded as 111.

## Slide 124
The first line of the truth table:
If ST NOT is 1, the priority encoder is not working.
The second line of the truth table :
If there is no encoding request of decimal numbers from 0 to 7 (I0,…,I7 NOT are 1),
encoding results Y are 111,
and Ys is 0.
It means no input signal.

## Slide 125
The third line of the truth table :
Decimal number 7 and maybe other numbers (their values are “d”) request encoding.
Decimal number 7 has the highest priority.
So decimal number 7 is encoded as 000 (inverting binary number 111).
The encoding result uses low-voltage.
YEX NOT is 0.
It means there are input signals.

## Slide 126
The fourth line of the truth table :
Decimal number 7 has no encoding request (I7 NOT is 1).
Decimal number 6 and maybe other numbers (d) request encoding.
Now, decimal number 6 has the highest priority.
So decimal number 6 is encoded as 001 (inverting binary number 110).

## Slide 127
If ST_NOT is 1, the encoder is disabled.
If all the inputs are 1, Ys is 0 (there is no input signal).
If I_7 NOT is 0, the decimal 7 is encoded as 000.
If I_0 NOT is 0, the decimal 0 is encoded as 111.
Notes

## Slide 128
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
ST I0 I1 I2 I3 I4 I5 I6 I7
0 1 1 1 1 1 1 1 1
YS=0
ST I0 I1 I2 I3 I4 I5 I6 I7
1 1 1 1 1 1 1 1 1
YS=0
YS=?

## Slide 129
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
ST I0 I1 I2 I3 I4 I5 I6 I7
1 d d d d d d d d
YEX=1
ST
1
ST I0 I1 I2 I3 I4 I5 I6 I7
0 1 1 1 1 1 1 1 1
YEX=1
YS=1
YEX=?

## Slide 130
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
Y2=?

## Slide 132
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
Y1=?

## Slide 134
ST I0 I1 I2 I3 I4 I5 I6 I7 Y2 Y1 Y0 YEX YS
1 d d d d d d d d 1 1 1 1 1
0 1 1 1 1 1 1 1 1 1 1 1 1 0
0 d d d d d d d 0 0 0 0 0 1
0 d d d d d d 0 1 0 0 1 0 1
0 d d d d d 0 1 1 0 1 0 0 1
0 d d d d 0 1 1 1 0 1 1 0 1
0 d d d 0 1 1 1 1 1 0 0 0 1
0 d d 0 1 1 1 1 1 1 0 1 0 1
0 d 0 1 1 1 1 1 1 1 1 0 0 1
0 0 1 1 1 1 1 1 1 1 1 1 0 1
Y0=?

## Slide 137: Exercise

## Slide 138
Write the truth table of the priority encoder.

## Slide 139: 4.3.5 Decoder
X1
Xn
Y1
Y2n
Decoder
n－2n
Decoder coverts a binary number to the equivalent decimal number.
A0
A1
Z0
Z1
Z2
2-4
Decoder
Z3
Notes: The binary numbers with n bits are decoded into the nth power of two decimal numbers.
For the 2 to 4 decoder, the binary numbers with 2 bits are decoded into 4 decimal numbers.
If all the binary numbers can be decoded, it is called the complete decoder.
For the decoder, we have n inputs and nth power of 2 outputs.
For the 2-4 decoder, we have 2 inputs and 4 outputs.

## Slide 140
The decoder converts binary numbers to decimal numbers.
A n-bit binary number is converted to one of the n th power of 2 decimal numbers.
Look at the 2 to 4 decoder.
The input is a 2-bit binary number.
The outputs are decimal numbers from 0 to 3.
The outputs use low-level voltage.
We use inverter to indicate the low-level voltage output.
Notes

## Slide 141
The binary numbers with n bits are decoded into the nth power of two decimal numbers.
For the 2 to 4 decoder, the binary numbers with 2 bits are decoded into 4 decimal numbers.
If all the binary numbers can be decoded, it is called the complete decoder.
Notes

## Slide 142
E A1 A0 Z3 Z2 Z1 Z0
0 d d 1 1 1 1
1 1 1 0 1 1 1
1 1 0 1 0 1 1
1 0 1 1 1 0 1
1 0 0 1 1 1 0
E= 1
then the chip works.
If
Truth Table for 2-4 Decoder
Notes: The outputs of the 2 to 4 decoder is low-level voltage effective.
The binary number 00 is decoded into decimal 0 (Z0_NOT is 0).
The binary number 11 is decoded into decimal 3 (Z3_NOT is 0).

## Slide 143
E A1 A0 Z3 Z2 Z1 Z0
0 d d 1 1 1 1
1 1 1 0 1 1 1
1 1 0 1 0 1 1
1 0 1 1 1 0 1
1 0 0 1 1 1 0

## Slide 144
Let’s look at the Truth Table of 2-4 decoder.
0 is the decoding signal for each binary number.
The binary number 00 is decoded as the decimal number 0.
The binary number 11 is decoded as the decimal number 3.
If E is 1, the decoder is working.
Notes

## Slide 145
The outputs of the 2 to 4 decoder is low-level voltage effective.
The binary number 00 is decoded into decimal 0 (Z0_NOT is 0).
The binary number 11 is decoded into decimal 3 (Z3_NOT is 0).
Notes

## Slide 146: Exercise

## Slide 147
Write the truth table of the 2-4 decoder.

## Slide 148
Convert 8421BCD Code to Decimal Number
2. 8421 BCD to Decimal Decoder
The 8421 BCD code which covers the binary numbers from 0000 to 1001, will be decoded.
The numbers from 1010 to 1111 will not be decoded.
Notes: For the binary to decimal decoder, we will convert the 8421 BCD code into the decimal numbers.
The 8421 BCD code which covers the binary number from 0000 to 1001, will be decoded.
The numbers from 1010 to 1111 will not be decoded.

## Slide 149
For the 8421 BCD to decimal decoder, we will convert the 8421 BCD code into the decimal numbers.
The 8421 BCD code which covers the binary number from 0000 to 1001, will be decoded.
Notes

## Slide 150
E A3 A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5 Z6 Z7 Z8 Z9
1 0 0 0 0 0 1 1 1 1 1 1 1 1 1
1 0 0 0 1 1 0 1 1 1 1 1 1 1 1
1 0 0 1 0 1 1 0 1 1 1 1 1 1 1
1 0 0 1 1 1 1 1 0 1 1 1 1 1 1
1 0 1 0 0 1 1 1 1 0 1 1 1 1 1
1 0 1 0 1 1 1 1 1 1 0 1 1 1 1
1 0 1 1 0 1 1 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 1 1 1 1 0 1 1
1 1 0 0 0 1 1 1 1 1 1 1 1 0 1
1 1 0 0 1 1 1 1 1 1 1 1 1 1 0
0 d d d d 1 1 1 1 1 1 1 1 1 1
Truth Table of 8421BCD to Decimal Decoder
Notes: The outputs of the binary to decimal decoder is low-level voltage effective.
The 8421 BCD code 0000 is decoded into decimal value 0 (Z0_NOT is 0).
The 8421 BCD code 1001 is decoded into decimal value 9 (Z9_NOT is 0).
If E is 0, the decoder is disabled. 0000 is decoded as 0. 1001 is decoded as 9.

## Slide 151
Let’s look at the Truth Table of 8421BCD to Decimal Decoder.
The last line of the truth table:
if E is 0, the decoder is not working.
All the outputs are 1.

## Slide 152
The first line of the truth table:
if E is 1, the decoder is working.
The 8421 BCD code 0000 is converted to decimal number 0.
The output uses low-level voltage.
The second line of the truth table:
The 8421 BCD code 0001 is converted to decimal number 1.

## Slide 153
The outputs of the 8421 BCD to decimal decoder is low-level voltage effective.
The 8421 BCD code 0000 is decoded into decimal value 0 (Z0_NOT is 0).
The 8421 BCD code 1001 is decoded into decimal value 9 (Z9_NOT is 0).
Notes

## Slide 155: Exercise

## Slide 156
Write the truth table of the 8421 BCD to decimal decoder.

## Slide 157
3. Use NAND gate to design a Seven-Segment Digital Display Decoder.
Convert the 8421BCD Code to seven LEDs.

## Slide 158
b
c
a
g
f
e
d
a
b
c
g
f
e
d
Input
a, b, c ,d, e, f, and g are Light Emitting Diodes (LED) lights.
In this case, high-level voltage makes the diode (LED) emit.
Seven-Segment
Digital Display
Notes: Seven-Segment Digital Display can show the digits from 0 to 9.
The number from 0 to 9 will be displayed by the lights a b c d e f g.

## Slide 159
Seven-Segment Digital Display can show the decimal numbers from 0 to 9.
Now, we want to convert 8421BCD code to decimal number on the display.
8421BCD Codes are inputs (B8B4B2B1).
Seven LEDs are outputs (a, b, c, d, e, f, g).

## Slide 160
a
g
b
f
c
d
e
a
b
c
d
e
f
g
B1
B2
B4
B8
a
b
c
d
e
f
g
74LS48
Seven-Segment Decoder
Inputs:
8421 BCD Code
Outputs:
7 LED lights
Notes: The inputs of Seven-Segment Digital Display Decoder are B8 B4 B2 B1.
The outputs of Seven-Segment Digital Display Decoder are a, b, c, d, e, f, g.
The inputs control the on and off state of the output lights.
We will decode the BCD code by the lights.

## Slide 161
The inputs of Seven-Segment Digital Display Decoder are B8 B4 B2 B1.
The outputs of Seven-Segment Digital Display Decoder are a, b, c, d, e, f, g.
The inputs control the on and off state of the output lights.
Notes

## Slide 162
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a
Truth Table of Seven-Segment Decoder
Notes: If B8, B4, B2, B1 are 0, we can see the digit 0 in the display.
The lights a, b, c, d, e, f are on.
The BCD code 0000 is decoded as 0 by the lights.

## Slide 163
If B8, B4, B2, B1 are 0, we can see the digit 0 in the display.
The lights a, b, c, d, e, f are on.
Notes

## Slide 164
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a

## Slide 165
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a

## Slide 166
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a

## Slide 167
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a

## Slide 168
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
b
c
d
e
f
g
a

## Slide 169
B8 B4 B2 B1 a b c d e f g Decimal
~
~
1 1 1 1 d d d d d d d
1 0 1 0 d d d d d d d
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6
b
c
d
e
f
g
a

## Slide 170
B8 B4 B2 B1 a b c d e f g Decimal
~
~
1 1 1 1 d d d d d d d
1 0 1 0 d d d d d d d
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6
b
c
d
e
f
g
a

## Slide 171
B8 B4 B2 B1 a b c d e f g Decimal
~
~
1 1 1 1 d d d d d d d
1 0 1 0 d d d d d d d
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6
b
c
d
e
f
g
a

## Slide 172
B8 B4 B2 B1 a b c d e f g Decimal
~
~
1 1 1 1 d d d d d d d
1 0 1 0 d d d d d d d
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6
b
c
d
e
f
g
a
For numbers from 1010 to 1111, the outputs are “d”.

## Slide 173
How to write the logic function of LED a?
8421BCD Codes are inputs (B8 B4 B2 B1).
LED a is the output.
Draw the K-map of function a.
Draw K-circles on “1” blocks.
Use NAND gate to implement function a.

## Slide 174
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6
Notes: How can we write the logic function of the light a?

## Slide 175
a
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
1
0
1
1
1
1
1
0
1
Notes: Draw the K-map of light a. Circle on “1”.

## Slide 176
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 177
b
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
1
1
1
1
1
1
1
0
0
1

## Slide 178
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 179
c
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
1
1
1
1
1
0
1
1
1
1

## Slide 180
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 181
d
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
1
0
1
0
1
0
1
1
1

## Slide 182
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 183
e
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
0
0
1
0
1
0
0
1
1

## Slide 184
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 185
f
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
0
1
1
1
0
0
1
1
1

## Slide 186
B8 B4 B2 B1 a b c d e f g Decimal
0 1 0 1 1 0 1 1 0 1 1 5
0 1 0 0 0 1 1 0 0 1 1 4
0 0 1 1 1 1 1 1 0 0 1 3
0 0 1 0 1 1 0 1 1 0 1 2
0 0 0 1 0 1 1 0 0 0 0 1
0 0 0 0 1 1 1 1 1 1 0 0
1 0 0 1 1 1 1 0 0 1 1 9
1 0 0 0 1 1 1 1 1 1 1 8
0 1 1 1 1 1 1 0 0 0 0 7
0 1 1 0 0 0 1 1 1 1 1 6

## Slide 187
g
B8B4
B2B1
00
00
01
01
11
11
10
10
d
d
d
d
d
d
0
1
1
1
1
1
0
1
1
0

## Slide 188
Output Functions of LEDs

## Slide 189: Exercise

## Slide 190
1: Write the truth table of the 7-segment decoder, which converts the 8421 BCD to LEDs.
2: Write the K-maps of the 7-segment decoder.
Write the simplest functions from the K-maps.

## Slide 191
4. Application of Decoder
(Chip Serial 74LS138)
0
0
1
A0
A1
A2
S3
S2
S1
Z7
Z6
Z5
Z4
Z3
Z2
Z1
Z0
VCC
1
8
9
16
Ground
74LS138
3-8 Decoder
Pin diagram of 3-8 Decoder
Notes: For the 3 to 8 decoder, the binary number with 3 bits are decoded into decimal numbers from 0 to 7.
For the control pins, the S3_NOT is 0, S2_NOT is 0, and S1 is 1.
S3, S2 and S1 are the control pins.

## Slide 192
For the 3 to 8 decoder, the binary number with 3 bits are decoded into decimal numbers from 0 to 7.
For the control pins, the S3_NOT is 0, S2_NOT is 0, and S1 is 1.
Notes

## Slide 193
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 194
The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
Notes

## Slide 195
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 196
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 197
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 198
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 199
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 200
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 201
A2 A1 A0 Z0 Z1 Z2 Z3 Z4 Z5Z6Z7
0 0 0 0 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 0
0 0 1 1 0 1 1 1 1 1 1
0 1 0 1 1 0 1 1 1 1 1
0 1 1 1 1 1 0 1 1 1 1
1 0 0 1 1 1 1 0 1 1 1
1 0 1 1 1 1 1 1 0 1 1
1 1 0 1 1 1 1 1 1 0 1
Truth Table of 3-8 Decoder
Notes: The outputs are low-level voltage effective.
The binary number 000 is decoded into the decimal number 0 (Z0_NOT is 0).
The binary number 111 is decoded into the decimal number 7 (Z7_NOT is 0).
000 is decoded as 0. 111 is decoded as 7.
Write the minterm of each row. Invert the minterm. Then, we get the Z expression.

## Slide 202
Write the inputs (A2 A1 A0) by numbered minterms.
Output Functions of 3-8 Decoder
Notes: We can rewrite the input variables in the form of minterms.
Rewrite the functions by minterm in number.
000 is m0.

## Slide 203
We can rewrite the input variables in the form of numbered minterms.
So we can apply the 3-8 Decoder to implement any logic functions.

## Slide 204: Exercise

## Slide 205
1: Write the truth table of the 3-8 decoder.
2: Write the functions of the 3-8 decoder.

## Slide 206
Example: Apply 3-8 Decoder（74LS138）to implement logic functions.
Notes: We will try to get all the minterms of each function.

## Slide 207
First, we recover all the minterms of each function.

## Slide 208
Notes: Expand each product term into minterm.
Get the minterm number.

## Slide 209
All the functions are in the form of inverted minterms.
Notes: The minterm is in the inverted relation to the maxterm.
Remove the invertor on minterm. We get the maxterm.

## Slide 210
Z0
Z1
Z2
Z3
Z4
Z5
Z6
Z7
A0
A1
A2
S1
S2
S3
“1”
A
B
C
Z1
Z2
Z3
Z4
74LS138
Notes: We can draw the pin diagram of the 3 to 8 decoder.
The inputs of the function are A, B, C, which are connected to A2, A1, A0.
Set the control inputs. S3_NOT is 0, S2_NOT is 0, and S1 is 1.
For each function, we use the NAND gate to connect all the inverted minterms.
Connect the inverted minterms by NAND gate. Connect the input variables. Connect the control pins.
So the function is implemented by 3 to 8 decoder.

## Slide 211
We can draw the pin diagram of the 3 to 8 decoder.
The inputs of the function are A, B, C, which are connected to A2, A1, A0.
Set the control inputs. S3_NOT is 0, S2_NOT is 0, and S1 is 1.
For each function, we use the NAND gate to connect all the inverted minterms.
Notes

## Slide 212: Exercise

## Slide 213
Apply 3-8 Decoder（74LS138）to implement logic functions. Draw the circuit diagram.

## Slide 214
Ai Bi Gi-1 Di Gi
0 0 0 0 0
0 0 1 1 1
0 1 0 1 1
0 1 1 0 1
1 0 0 1 0
1 0 1 0 0
1 1 0 0 0
1 1 1 1 1
Apply 3-8 Decoder（74LS138）to implement the full subtractor. Draw the circuit diagram.

## Slide 215
Ai Bi Gi-1 Di Gi
0 0 0 0 0
0 0 1 1 1
0 1 0 1 1
0 1 1 0 1
1 0 0 1 0
1 0 1 0 0
1 1 0 0 0
1 1 1 1 1

## Slide 216
Z0
Z1
Z2
Z3
Z4
Z5
Z6
Z7
A0
A1
A2
S1
S2
S3
“1”
Ai
Bi
Gi-1
74LS138
Di
Gi

## Slide 217: 4.3.6 Data selector
4-to-1 Line
Data
selector
D0
D1
D2
D3
A1
A0
S
Y
D0
D1
D2
D3
A1
A0
Y
0 0
Notes: This is 4-to-1 line data selector.
S_NOT is the enabling pin.
A1 A0 are the address pins, ranging from 00 to 11.
Y is the output.
D0, D1, D2, D3 are the data, which will be selected by the address and sent to the output.
S is the control pin. D are data. A are address. Y is output.
Each time 1-of-4 Line is selected.

## Slide 218
This is 4-to-1 line data selector.
S_NOT is the enabling pin.
A1 A0 are the address pins, ranging from 00 to 11.
Y is the output.
D0, D1, D2, D3 are the data, which will be selected by the address and sent to the output.
Notes

## Slide 219
A1 A0 Y
1 1 D3
0 0 D0
0 1 D1
1 0 D2
Truth Table of 4-to-1 Line Data Selector
Notes: If S_NOT is 0, the data selector is working.
If A1 A0 are 00, data D0 is selected and sent to the output Y.
If A1 A0 are 01, data D1 is selected and sent to the output Y.
If A1 A0 are 10, data D2 is selected and sent to the output Y.
If A1 A0 are 11, data D3 is selected and sent to the output Y.
If we combine all the four conditions, we get the logic function of the data selector.
Write the minterm in each row. Then we get the Y expression.

## Slide 220
If S_NOT is 0, the data selector is working.
If A1 A0 are 00, data D0 is selected and sent to the output Y.
If A1 A0 are 01, data D1 is selected and sent to the output Y.
If A1 A0 are 10, data D2 is selected and sent to the output Y.
If A1 A0 are 11, data D3 is selected and sent to the output Y.
If we combine all the four conditions, we get the logic function of the data selector.
Notes

## Slide 221: Exercise

## Slide 222
1: Write the truth table of the 4-to-1 line data selector.
2: Write the function of the 4-to-1 line data selector.

## Slide 223
D0
D1
D2
D3
A0
A1
S
Y’
G
G
G
1
R
A
D0
D1
D2
D3
Y’
R A G Y
0 0 0 1
0 0 1 0
0 1 0 1
1 1 1 1
1 1 0 1
1 0 1 1
1 0 0 0
0 1 1 0
Example 1: Use the 4-to-1 Line Data Selector to implement the following truth table.

## Slide 224
C
1
1
1
1
1
AB
00
01
10
11
0
1
Y
Example 2: Use the 4-to-1 Line Data Selector to implement the following Logic Function.
Different K-map!
Notes: Method 1 is to use the K-map.
First, we will recover all the minterms of the function and put them into the K-map.
Please note that the K-map that we use to implement the data selector is different to those in Chapter Two.
We put the highest inputs AB in the horizontal direction and put the lowest input C in the vertical direction.

## Slide 225
Use K-map to find the data D0, D1, D2, D3.
First, we will recover all the minterms of the function and put them into the K-map.
Please note that the K-map that we use to implement the data selector is different to those in Chapter Two.
We put the highest inputs AB in the horizontal direction and put the lowest input C in the vertical direction.
Notes

## Slide 226
C
1
1
1
1
1
AB
00
01
10
11
0
1
Y
Different K-circle!
Notes: Then, we will draw K-circles and keep the address AB complete.
So we draw K-circles in each column independently.
Arrange the address AB in the ascending order, 00, 01, 10, 11.

## Slide 227
Then, we will draw K-circles and keep the address AB complete.
So we draw K-circles in each column independently.
Arrange the address AB in the ascending order, 00, 01, 10, 11.
Notes

## Slide 228
D0
D1
D2
D3
A0
A1
Y
C
C
C
1
A
B
S
0
Notes: By comparing the function that we get from the K-map, with the standard function of the data selector,
we find that D0 is C NOT, D1 is 1, D2 is C NOT, D3 is C.

## Slide 229
By comparing the function that we get from the K-map, with the standard function of the data selector,
we find that D0 is C NOT, D1 is 1, D2 is C NOT, D3 is C.
Notes

## Slide 230
F1(A，B，C，D)=∑m(0，1，5，7，10，13，15)
F2(A，B，C，D)=∑m(8，10，12，13，15)
Example 3: Use the 4-to-1 Line Data Selector to implement the following Logic Functions.
Notes: The function is given in the from of minterms.

## Slide 231
The function is given in the from of minterms.
Notes

## Slide 232
F1
AB
CD
00
00
01
01
11
11
10
10
0
1
1
0
1
0
1
0
0
0
0
0
1
1
0
1
F1(A，B，C，D)=∑m(0，1，5，7，10，13，15)
Notes: We draw the K-map of the function.
Put the highest inputs AB in the vertical direction.
Put the lowest inputs CD in the horizontal direction.
The highest inputs AB are the address pins.

## Slide 233
We draw the K-map of the function.
Put the highest inputs AB in the vertical direction.
Put the lowest inputs CD in the horizontal direction.
The highest inputs AB are the address pins.
Notes

## Slide 234
F1
AB
CD
00
00
01
01
11
11
10
10
0
1
1
0
1
0
1
0
0
0
0
0
1
1
0
1
F1(A，B，C，D)=∑m(0，1，5，7，10，13，15)
Notes: Draw the K-circles and keep the address AB complete.
Draw K-circles in each row independently.
Arrange the address of the function in the ascending order, 00, 01, 10, 11.

## Slide 235
Draw the K-circles and keep the address AB complete.
Draw K-circles in each row independently.
Arrange the address of the function in the ascending order, 00, 01, 10, 11.
Notes

## Slide 236
F2(A，B，C，D)=∑m(8，10，12，13，15)
F2
AB
CD
00
00
01
01
11
11
10
10
1
1
1
0
1
0
0
0
0
1
0
0
0
0
0
0

## Slide 237
F2(A，B，C，D)=∑m(8，10，12，13，15)
F2
AB
CD
00
00
01
01
11
11
10
10
1
1
1
0
1
0
0
0
0
1
0
0
0
0
0
0
Notes: Combine different items with the same address.
Change the OR gate into the NAND gate.

## Slide 238
Combine different items with the same address.
Change the OR gate into the NAND gate.
Notes

## Slide 239
Notes: Determine the data pins D0,…,D3.

## Slide 240
Determine the data pins D0,…,D3.
Notes

## Slide 241: Exercise

## Slide 242
F1(A，B，C，D)=∑m(0，1，5，7，10，13，15)
F2(A，B，C，D)=∑m(8，10，12，13，15)
Use the 4-to-1 Line Data Selector to implement the following Logic Functions. Draw the circuit diagram.

## Slide 243: 4.4 Hazard of Combinational Logic Circuit 4.4.1 Reasons of Race and Hazard
In digital circuits, as long as any two input signals change into the opposite direction simultaneously (i.e. from 01 into 10, or vice versa), the output of the gate may interfere with a pulse.
The two input signals changing into the opposite logic level at the same time is named as the race; the output error caused by the race is named as the hazard.

## Slide 244
race
hazard
Theoretically,
Notes: Theoretically, the output A dot A NOT equals 0.
But due to the time delay of the logic gates, the output A dot A NOT is 1 in some period.

## Slide 245
Theoretically, the output A dot A NOT equals 0.
But due to the time delay of the logic gates, the output A dot A NOT is 1 in some period.
Notes

## Slide 246: 4.4.2 Why do we need to detect Hazard?
Hazard causes the logical error of the circuit output for a moment.

## Slide 247: 4.4.3 How to detect a Hazard?
1. Assign values to input variables and find
Example:
Assign input values: B=C=1，
There is a Hazard.
Add the redundant term BC to eliminate Hazard. (The redundant term is always 1, when B and C are 1.)
Notes: The way to discover and avoid Hazard.
The method for discovering Hazard is to assign variables with constant values and get the form A plus A NOT, or A dot A NOT.
The method for avoiding Hazard is to add the redundant term.
In the function, we have the primitive variable A and the inverted variable A NOT, so we can add the redundant term BC.

## Slide 248
The Hazard is eliminated.

## Slide 249
The method for the detection of Hazard is to assign variables with constant values and get the form A plus A NOT, or A dot A NOT.
The first method for the elimination of Hazard is to add the redundant term.
In the function, we have the primitive variable A and the inverted variable A NOT, so we can add the redundant term BC.
Notes

## Slide 250: Exercise

## Slide 251
Detect and eliminate the hazard of the function.