## Slide 1: Chapter 6 Synchronous Sequential Logic Circuit
6.1 Definition of Synchronous Sequential Logic Circuit
6.2 Analysis of Synchronous Sequential Logic Circuit
6.3 Design of Synchronous Sequential Logic Circuit
6.4 Typical Synchronous Sequential Logic Circuits
Notes: Definition of Synchronous Sequential Circuit.
Analysis of Synchronous Sequential Circuit.
Design of Synchronous Sequential Circuit.
Typical Synchronous Sequential Circuits.

## Slide 2
Combinational
Logic Circuit
Flip-Flop
X(tn)
Y(tn)
Z(tn)
Q(tn)
tn：time step
X(tn)：input
Y(tn)：output
Q(tn)：present state
Z(tn)：excitation input

## Slide 3
We use Output Equation, Excitation Equation, and State Equation to describe the relationship between signal and time in sequential logic circuit.
What are Output Equation, Excitation Equation, and State Equation?
Let’s study them in an example.

## Slide 4
J
Q
Q
K
CP
X
Y
1
Output Equation:
Excitation Equation:
State Equation:
falling edge triggered
Characteristic Equation
of J-K Flip-Flop:
Example: Analyze the sequential logic circuit.
Notes: Example: Analyze the sequential logic circuit.
Recall the characteristic equation of JK flip-flop.
Q next state equals J dot Q current state inverter plus K inverter dot Q current state.
Y is the output of the circuit. Look at the gate. It is AND gate. Y equals X dot Q’s current state. This is output equation.
JK are the inputs of the flip-flop. J equals X dot Q’s current state inverter. K equals 1. This is excitation equation.
Take J and K into the characteristic equation. Write Q NOT once. K is 1. K NOT is 0. We get state equation.
Q’s next state equals X dot Q’s current state inverter.
The JK flip-flop is triggered by falling edge.

## Slide 5: 6.1 Definition of Synchronous Sequential Logic Circuit
The same clock pulse CP controls all the flip-flops at the same time.
What is a Synchronous Sequential Circuit?
Q1
Q1
D1
Q2
Q2
D2
Q3
Q3
D3
CP
X
Notes: Definition of Synchronous Sequential Circuit.
What is a Synchronous Sequential Circuit?
The same clock CP controls all the flip-flops at the same time.

## Slide 6
Q
Q
D
Q
Q
D
Q
Q
D
CP
asynchronous sequential logic

## Slide 7
Moore:
J
Q
Q
K
CP
X
Y
Y(tn)=F[Q(tn)]

## Slide 8
Y(tn)=F[X(tn) ，Q(tn)]
Mealy:
J
Q
Q
K
CP
X
Y

## Slide 9
（1）Moore： Y(tn)= F[Q(tn)]
（2）Mealy： Y(tn)= F[X(tn) ，Q(tn)]
Output function:

## Slide 10: 6.2 Analysis of Synchronous Sequential Logic Circuit 6.2.1 Steps for Analysis
2.Output Equation, Excitation Equation, State Equation
3.State Transition Table
4.State Transition Diagram
5.Role of the Circuit
1.Characteristic Equation of Flip-Flop
Notes: Analysis of Synchronous Sequential Circuit. Steps for Analysis.
Step one, write the characteristic equation of flip-flop.
Step two, write output equation, excitation equation, state equation.
Step three, write state transition table.
Step four, draw state transition diagram.
Step five, describe the role of the circuit.

## Slide 11: 6.2.2 Examples of Circuit Analysis
D3
Q3
Q3
CP
D2
Q2
Q2
D1
Q1
Q1
Z
Example 1
(1)
Output Equation :
Excitation Equation :
State Equation :
Characteristic Equation of D Flip-Flop:
Notes: Examples of Circuit Analysis. Example 1.
Recall the characteristic equation of D flip-flop. Q next state equals D.
D is the input of the flip-flop. D1 is Q3 inverter. D2 is Q1. D3 is Q1 dot Q2.
Take D into the characteristic equation. Write the state equation. Q1’s next state equals Q3’s current state inverter.
Z is the output of the circuit. Write the output equation. Z equals Q1 NOT dot Q3 inverter.

## Slide 12
Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
(2) State Transition Table
0 0 0 0 0 1
0 0 1 0 1 1 1
0 1 0 0 0 1 1
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 1 0 1 0 1
1 1 0 0 0 0 0
1 1 1 1 1 0 1
1
Notes: Write state transition table.
Current states are input signals. Next states are output signals. Z is the circuit output.
Write Q3 Q2 Q1. We write Q3 on the far left. Because Q3 is the highest bit.
Write the current state values of Q in the ascending order, from 000 to 111.
Calculate the next state values of Q by state equation.
Look at the first line. Current state Q3Q2Q1 are 0. For Q3’s next state, 0 dot 0 equals 0. Q3’s next state is 0.
Calculate circuit output Z by output equation.
Look at the first line. Current state Q3Q2Q1 are 0. For circuit output Z, Q3 is 0. Inverting 0 is 1.So Z is 1.

## Slide 13
State Transition Diagram：
Q3Q2Q1
/ Z
/ Z
Q3Q2Q1
……
The present state
The next state
Notes: State Transition Diagram.
Write each state value of Q3Q2Q1 in a circle. Use an arrow to connect the current state and next state.
Write the circuit output Z beside the arrow.

## Slide 14
010
101
/1
/1
011
/1
111
/1
110
/1
000
001
/1
/0
100
/0
(3) State Transition Diagram
Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
0 0 0 0 0 1 1
0 0 1 0 1 1 1
0 1 0 0 0 1 1
0 1 1 1 1 1 1
1 0 0 0 0 0 0
1 0 1 0 1 0 1
1 1 0 0 0 0 0
1 1 1 1 1 0 1
Role of circuit: it is a circuit counting five numbers.
Notes: Look at the first line of the state transition table.
The current state is 000. The next state is 001. The circuit output Z is 1.
If the current state is 110, and the next state is 000, then the circuit output Z is 0.
After we count five numbers, the circuit output becomes 0.
For role of the circuit, it is a circuit counting five numbers.

## Slide 15: Exercise

## Slide 16: Analyze the circuit (write the equation, state table, state diagram, role).
D3
Q3
Q3
CP
D2
Q2
Q2
D1
Q1
Q1
Z
Notes: Examples of Circuit Analysis. Example 1.
Recall the characteristic equation of D flip-flop. Q next state equals D.
D is the input of the flip-flop. D1 is Q3 inverter. D2 is Q1. D3 is Q1 dot Q2.
Take D into the characteristic equation. Write the state equation. Q1’s next state equals Q3’s current state inverter.
Z is the output of the circuit. Write the output equation. Z equals Q1 NOT dot Q3 inverter.

## Slide 17
Example 2
J1
Q1
Q1
K1
J2
Q2
Q2
K2
J3
Q3
Q3
K3
CP
Y
1

## Slide 18
(1)
Output Equation:
Excitation Equation:
J1
Q1
Q1
K1
J2
Q2
Q2
K2
J3
Q3
Q3
K3
CP
Y
1

## Slide 19
Output Equation :
Excitation Equation :
State Equation :

## Slide 20
Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Y
0 0 1 0 1 0 0
0 1 0 0 1 1 0
0 1 1 1 0 0 0
1 0 0 1 0 1 0
1 0 1 1 1 0 0
1 1 0 0 0 0 1
1 1 1 0 0 0 1
0 0 0 0 0 1 0
(2) State Transition Table

## Slide 21
000
001
010
011
100
101
110
111
/0
/0
/0
/0
/0
/0
/1
/1
(3) State Transition Diagram
Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Y
0 0 1 0 1 0 0
0 1 0 0 1 1 0
0 1 1 1 0 0 0
1 0 0 1 0 1 0
1 0 1 1 1 0 0
1 1 0 0 0 0 1
1 1 1 0 0 0 1
0 0 0 0 0 1 0
Role of circuit: it is a circuit counting seven numbers.

## Slide 22: Exercise

## Slide 23: Analyze the circuit (write the equation, state table, state diagram, role).
J1
Q1
Q1
K1
J2
Q2
Q2
K2
J3
Q3
Q3
K3
CP
Y
1

## Slide 24
Example 3
J2
Q2
Q2
K2
J1
Q1
Q1
K1
Y
X
CP
1
1

## Slide 25
(1)
J2
Q2
Q2
K2
J1
Q1
Q1
K1
Y
X
CP
Output Equation:
Excitation Equation:
State Equation:
J-K Flip-Flop
OR Gate
J=1，K=1，
Flip
1
1

## Slide 26
Hint: Change NAND Gate into OR Gate
Prove the formula by De Morgan’s law.

## Slide 27
X Q2n Q1n Q2n+1 Q1n+1 Y
(2) State Transition Table
0 0 0 0 1 0
0 0 1 1 0 0
0 1 0 1 1 0
0 1 1 0 0 1
1 0 0 1 1 1
1 0 1 0 0 0
1 1 0 0 1 0
1 1 1 1 0 0
Input

## Slide 28
00
01
10
11
X/Y
0/0
1/1
1/0
1/0
1/0
0/0
0/0
0/1
(3) State Transition Diagram
X Q2n Q1n Q2n+1 Q1n+1 Y
0 0 0 0 1 0
0 0 1 1 0 0
0 1 0 1 1 0
0 1 1 0 0 1
1 0 0 1 1 1
1 0 1 0 0 0
1 1 0 0 1 0
1 1 1 1 0 0
Role of circuit:
it is a circuit counting four numbers by addition or subtraction.

## Slide 29: Exercise

## Slide 30: Analyze the circuit (write the equation, state table, state diagram, role).
J2
Q2
Q2
K2
J1
Q1
Q1
K1
Y
X
CP
1
1

## Slide 31
Example 4:
Q2
Q2
D
Q1
Q1
CP
X
Z
D
(1)
Output Equation:
Excitation Equation:
State Equation:

## Slide 32
X Q2n Q1n Q2n+1 Q1n+1 Z
0 0 0 0 0 0
0 0 1 1 0 0
0 1 0 0 0 0
0 1 1 0 0 0
1 0 0 0 1 0
1 0 1 0 1 0
1 1 0 0 1 1
1 1 1 0 1 0
(2) State Transition Table

## Slide 33
00
01
10
11
X/Z
0/0
1/0
1/0
0/0
0/0
1/1
0/0
1/0
Overlapped “101” Sequence
Detector
X=100101011101000101
Z=000001010001000001
X Q2n Q1n Q2n+1 Q1n+1 Z
0 0 0 0 0 0
0 0 1 1 0 0
0 1 0 0 0 0
0 1 1 0 0 0
1 0 0 0 1 0
1 0 1 0 1 0
1 1 0 0 1 1
1 1 1 0 1 0
(3) State Transition Diagram

## Slide 34: 6.3 Design of Synchronous Sequential Logic Circuit
(1) State Transition Diagram
(2) State Transition Table
(5) Circuit Diagram
6.3.1 Design Steps
(3) Simplification of Output Equation and State Equation by K-map
(4) Excitation Equation
Notes: Design of Synchronous Sequential Circuit. Design Steps.
Step one, draw State Transition Diagram.
Step two, write State Transition Table.
Step three, simplify the state equation and output equation by K-map.
Step four, write Excitation Equation by Output Equation.
Step five, draw Circuit Diagram.

## Slide 35: 6.3.2 State Simplification
The state transition table is divided into two categories.
If the output variable or the next state variable is “d” (“don’t care term”), the state transition table is “in-completely specified”.
Otherwise, the state transition table is “completely specified”.

## Slide 36
S2
S1
Sn
1/0
1/0
0/0
0/0
Given the same inputs, if both states “Si” and “Sj” have the same outputs and the same (or equivalent) next states, “Si” and “Sj” are the equivalent state pair.
We use the equivalent state pairs to simplify the completely specified state transition table.
1. Equivalent state

## Slide 37
(S1，S2)，(S2，S3) (S1，S2，S3)
Suppose that “Si” and “Sj” are the equivalent state pair, “Sj” and “Sn” are also the equivalent state pair.
Therefore, “Si” and “Sn” are the equivalent state pair.
Furthermore, “Si”, “Sj” and “Sn” constitute the equivalent state class.
This is the “transitivity” of the equivalent state pair.

## Slide 38
Sj
Si
Sn
1/0
0/0
1/0
0/0
Case 1
Sj
Si
0/1
1/0
1/0
0/1
Case 2
Specifically, “Si” and “Sj” are the equivalent state pair, if one of the four conditions is met as follows.

## Slide 39
Sj
Si
Sl
Sk
Sn
0/1
1/0
0/1
1/0
0/1
1/0
0/1
1/0
Case 3
Sj
Si
1/0
0/0
1/0
0/0
Case 4

## Slide 40
Example: Simplify the completely specified state transition table by the implication chart method.
Next state / Output
Present
state
A C/0 B/1
B F/0 A/1
C D/0 G/0
D D/1 E/0
E C/0 E/1
F D/0 G/0
G C/1 D/0
X=0 X=1

## Slide 41
A
B
C
D
E
F
B
C
D
E
F
G
Implication chart

## Slide 42
A
B
C
D
E
F
B
C
D
E
F
G
CF
BE
AE
CF
×
×
×
×
×
×
×
×
×
×
×
×
√
×
×
×
DE
CD
×

## Slide 43
AE BE CF √
DG CD ×
DE ×
A
B
C
D
E
F
B
C
D
E
F
G
CF
BE
AE
CF
×
×
×
×
×
×
×
×
×
×
×
×
√
×
×
×
DE
CD
×

## Slide 44
A
B
C
D
E
F
B
C
D
E
F
G
CF
BE
AE
CF
×
×
×
×
×
×
×
×
×
×
×
×
√
×
×
×
DE
CD
×

## Slide 45
(A，B) ， (A，E) ， (B，E) ， (C，F)
｛(A，B，E)，(C，F)，(D)，(G)｝
4 equivalent state pairs from the implication chart
4 equivalent state classes

## Slide 46
(A，B，E)，(C，F)，(D)，(G) 
a、b、c、d
Next state/Output
X=0 X=1
d b/1 c/0
c c/1 a/0
b c/0 d/0
a b/0 a/1
Present
state

## Slide 47
2. Compatible state
Given the same inputs, if both states “Si” and “Sj” have the same (or compatible) outputs and the same (or compatible) next states, “Si” and “Sj” are the compatible state pair.
We use the compatible state pairs to simplify the in-completely specified state transition table.

## Slide 48
Sj
Si
Sn
input/output
Case 1
Specifically, “Si” and “Sj” are the compatible state pair, if one of the four conditions is met as follows.
input/output

## Slide 49
Sj
Si
Case 2
input/output
input/output

## Slide 50
Sj
Si
Sl
Sk
Sn
Case 3
input/output
input/output
input/output
input/output

## Slide 51
Sj
Si
Case 4
input/output
input/output

## Slide 52
Next state
X=0 X=1 Output
A B D 0
B B D d
C A E 1
D d E 1
E F d 1
F d C d
Example: Simplify the in-completely specified state transition table by the implication chart method.
Present
state

## Slide 53
A
B
C
D
E
B
C
D
E
F
AF
BF
CE
CD
AB
DE
×
×
×
√
√
DE
CD
CE
√
√

## Slide 54
AF CD√
BD DE√
BE BF CD√
DE√
BC AB√
A
B
C
D
E
B
C
D
E
F
AF
BF
CE
AB
CD
DE
×
×
×
√
√
DE
CD
CE
√
√
BF CD√
CE AF CD√
CF CE√
DF CE√

## Slide 55
(A，B)，(A，F)，(B，C)，(B，D)，(B，E)
(B，F)，(C，D)，(C，E)，(C，F)，(D，E)
(D，F)，(E，F)
12 compatible state pairs from the implication chart

## Slide 56
D
E
F
A
B
C
(A，B)，(A，F)，(B，C)
(B，D)，(B，E)，
(B，F)
(C，D)，(C，E)，(C，F)
(D，E)，
(D，F)，(E，F)
(A，B，F)
(B，C，D，E，F)
2 compatible state classes

## Slide 57
Closure
Coverage
A B C D E F X=0 X=1
A B F A B F B CD
B C D E F B C D E F ABF CDE
(A，B，F)
(B，C，D，E，F)
Compatible
state class

## Slide 58
C‘(B，C，D，E，F)
A‘(A，B，F)
Next state
X=0 X=1
A’ A’,C’ C’ 0
C’ A’ C’ 1
Output
Present
state

## Slide 59
Next state
X=0 X=1
A’ d C’ 0
C’ A’ C’ 1
Output
Present
state

## Slide 60: 6.3.3 Counter
It counts the number of rising edges ( ) or falling edges ( ) of the clock pulse (CP).
It depends on the flip-flop.
The D flip-flop is triggered by the rising-edge.
The J-K flip-flop is triggered by the falling-edge.

## Slide 61
Example 1:
Design the subtraction counter for the 2-bit binary numbers by T flip-flop.
The working mode of the subtraction counter is controlled by the input variable “X”.
If the input variable “X” is “0”, the subtraction counter enters into the “keeping” mode.
If the input variable “X” is “1”, the subtraction counter is working.
The subtraction counter has one output variable “Z”.
If the subtraction counter generates the borrow, the output variable “Z” is “1”.
Otherwise, the output variable “Z” is “0”.

## Slide 62
00
01
10
11
0/0
1/0
0/0
1/0
0/0
1/0
0/0
1/1
1. State Transition Diagram

## Slide 63
X Q2n Q1n Q2n+1 Q1n+1 Z
0 0 0 0 0 0
0 0 1 0 1 0
0 1 0 1 0 0
0 1 1 1 1 0
1 0 0 1 1 1
1 0 1 0 0 0
1 1 0 0 1 0
1 1 1 1 0 0
2. State Transition Table

## Slide 64
X
Q2nQ1n
00
01
11
10
0
1
0
1
0
0
0
1
1
1
Q2n+1
X
Q2nQ1n
00
01
11
10
0
1
0
1
0
1
1
0
1
0
Q1n+1
3. Simplification by K-map

## Slide 65
X
Q2n Q1n
00
01
11
10
0
1
0
0
0
0
0
0
1
0
Z
T Flip-Flop

## Slide 66
T
Q1
Q1
T
Q2
Q2
CP
X
Z
4. Circuit Diagram

## Slide 67
Example 2: Design the addition-or-subtraction counter for three binary numbers by J-K Flip-Flops.
The input X=0 means the circuit is acting as the addition counter, and X=1 means the circuit is acting as the subtraction counter.
If there is a carry or borrow, then the output Z=1. Otherwise, Z=0.

## Slide 68
00
01
10
1/0
1/1
1/0
0/0
0/0
0/1
1. State Transition Diagram
State 11 is unused.
X=0 addition counter
X=1 subtraction counter
Notes: Draw State Transition Diagram.
If the input is 1, the circuit is acting as the addition counter.
00 plus 1 equals 01. No borrow. The output is 0.
If the input is 0, the circuit is acting as the subtraction counter.
10 minus 1 equals 01. No borrow. The output is 0.
Pay attention. State 11 is unused.

## Slide 69
X Q2n Q1n Q2n+1 Q1n+1 Z
0 0 0 0 1 0
0 0 1 1 0 0
0 1 0 0 0 1
0 1 1 d d d
1 0 0 1 0 1
1 0 1 0 0 0
1 1 0 0 1 0
1 1 1 d d d
2. State Transition Table
State 11 is unused.
X=1 subtraction counter
X=0 addition counter
Notes: Write State Transition Table.
We have circuit input X, current state, next state, and circuit output Z.
We write Q2 on the far left. Because Q2 is the highest bit.
If x is 0, it is the subtraction counter. If x is 1, it is the addition counter.
Pay attention. State 11 is unused. So the next state of 11 is dd. The output of 11 is d.
d is the don’t care term.

## Slide 70
X
Q2nQ1n
00
01
11
10
0
1
0
d
0
0
1
0
1
d
Q2n+1
X
Q2nQ1n
00
01
11
10
0
1
1
d
0
1
0
0
0
d
Q1n+1
J-K Flip-Flop:
3. Simplification by K-map
Notes: Simplify the state equation by K-map.
Look at the K-map of Q2’s next state.
Q2’current state has value 0 in shadow blocks. Q2’current state has value 1 in clear blocks.
The circuit is required to be implemented by JK flip-flop. So we need the form of Q2’current state in state equation.
And we need the form of Q2’current state inverter in state equation. This means we have to draw K-circles in shadow blocks and clear blocks independently. Extract Q2 inverter. Write the XOR form of X and Q1. We do not have Q2. So K2 is 1. J2 is X XOR Q1.

## Slide 71
X Q2n Q1n Q2n+1 Q1n+1 Z
0 1 1 0 0 0
1 1 1 0 0 0
X
Q2nQ1n
00
01
11
10
0
1
0
d
0
0
0
1
1
d
Z
Check the unused state 11.
The next state is valid (state 00). The output is correct (Z=0).
Draw K-circle on “1” blocks only.
Notes: Simplify the output equation by K-map. Draw K-circle on “1” blocks only. We get the output equation Z.
Check the unused state 11. The next state is valid (state 00). The output is correct (Z=0).

## Slide 72
X Q2n Q1n Q2n+1 Q1n+1 Z
0 1 1 0 0 1
1 1 1 0 0 0
X
Q2nQ1n
00
01
11
10
0
1
0
d
0
0
0
1
1
d
Z
Draw K-circle on “1” blocks and “d” blocks.
Check the unused state 11.
The next state is valid (state 00). The output is wrong (Z=1).
Notes: Simplify the output equation by K-map. Draw K-circle on “1” blocks and “d” blocks. We get the output equation Z.
The next state is valid (state 00). The output is wrong (Z=1).

## Slide 73: How to draw K-circles for output equation?
Draw the K-circle on “1” blocks only for output equation.
That is to say, don’t draw the K-circle on “d” blocks for output equation.
Otherwise, the output will be wrong.

## Slide 74
J1
Q1
Q1
J2
Q2
Q2
CP
X
Z
K1
K2
4. Circuit Diagram
Notes: Draw Circuit Diagram.

## Slide 75: Exercise

## Slide 76
Design the addition-or-subtraction counter for three binary numbers by J-K Flip-Flops.
The input X=0 means the circuit is acting as the addition counter, and X=1 means the circuit is acting as the subtraction counter.
If there is a carry or borrow, then the output Z=1. Otherwise, Z=0.

## Slide 77: 6.4 Examples of Typical Synchronous Sequential Logic Circuits 6.4.1 Integrated Counter
1
8
9
16
74LS161
CO
D0
VCC
Q3
Q1
Q2
Q0
LD
CTT
D3
D1
D2
CTP
CP
CR
Chip Pin Diagram of Four-Bit Binary Addition Counter 74LS161
Notes: Examples of Typical Synchronous Sequential Circuits. Integrated Counter.
This is the chip pin diagram of Four-bit binary addition counter 74LS161.
Connect the 8th pin to ground. Connect the 16th pin to voltage.

## Slide 78
1
8
9
16
74LS161
CO
D0
VCC
Q3
Q1
Q2
Q0
LD
CTT
D3
D1
D2
CTP
CP
CR
If CR NOT is 0, the counted number will be set to 0000 at once.
If LD NOT is 0, the counted number will be set to D3D2D1D0 when the next clock pulse (rising edge) triggers.
CP is clock pulse (rising edge triggered).
Notes: If CR NOT is 0, the counted number will be set to 0000 at once.
If LD NOT is 0, the counted number will be set to D3D2D1D0 when the next clock pulse (rising edge) triggers.
CP is clock pulse (rising edge triggered).

## Slide 79
1
8
9
16
74LS161
CO
D0
VCC
Q3
Q1
Q2
Q0
LD
CTT
D3
D1
D2
CTP
CP
CR
Q3Q2Q1Q0 is the counted number (output).
CO is the counting carry. CO is 1 when Q3Q2Q1Q0 changes from 1111 to 0000.
If CTP CTT is 11, the chip is acting as the addition counter. Otherwise, the counted number Q3Q2Q1Q0 is unchanged.
Notes: Q3Q2Q1Q0 is the counted number (output).
CO is the counting carry. CO is 1 when Q3Q2Q1Q0 changes from 1111 to 0000.
If CTP CTT is 11, the chip is acting as the addition counter. Otherwise, the counted number Q3Q2Q1Q0 is unchanged.

## Slide 80
CR LD CTP CTT CP D3 D2 D1 D0
0 d d d d d d d d 0 0 0 0 clear
1 1 0 d d d d d d
1 1 d 0 d d d d d
1 0 d d d3 d2 d1 d0 d3 d2 d1 d0 load
1 1 1 1 d d d d addition counter
keep
Function Table of Integrated Counter
The first line: If CR NOT is 0, the counted number will be set to 0000 (Q3Q2Q1Q0) at once.
Notes: Function Table of Integrated Counter.
The first line: If CR NOT is 0, the counted number will be set to 0000 at once.
The second line: If LD NOT is 0, the counted number will be set to D3D2D1D0 when the next clock pulse (rising edge) triggers.
The third line: If CTP CTT is 11, the chip is acting as the addition counter. Otherwise, the counted number Q3Q2Q1Q0 is unchanged (the 4th and 5th line).

## Slide 81
CR LD CTP CTT CP D3 D2 D1 D0
0 d d d d d d d d 0 0 0 0 clear
1 1 0 d d d d d d
1 1 d 0 d d d d d
1 0 d d d3 d2 d1 d0 d3 d2 d1 d0 load
1 1 1 1 d d d d addition counter
keep
Function Table of Integrated Counter
The second line: If LD NOT is 0, the counted number will be set to D3D2D1D0 when the next clock pulse (rising edge) triggers.

## Slide 82
CR LD CTP CTT CP D3 D2 D1 D0
0 d d d d d d d d 0 0 0 0 clear
1 1 0 d d d d d d
1 1 d 0 d d d d d
1 0 d d d3 d2 d1 d0 d3 d2 d1 d0 load
1 1 1 1 d d d d addition counter
keep
Function Table of Integrated Counter
The third line: If CTP CTT is 11, the chip is acting as the addition counter. Otherwise, the counted number Q3Q2Q1Q0 is unchanged (the 4th and 5th line).

## Slide 83
CP
D3 D2 D1 D0
LD
Q3 Q2 Q1 Q0
74LS161
CP
Example 1: Implement the addition counter ranging from 0000 to 1011 by the loading method.
D3D2D1D0 is 0000.
If Q3Q2Q1Q0 is 1011, the output of NAND gate is 0.
If LD NOT is 0, the counted number will be set to 0000 (D3D2D1D0) when the next clock pulse (rising edge) triggers.
Notes: D3D2D1D0 is 0000.
If Q3Q2Q1Q0 is 1011, the output of NAND gate is 0.
If LD NOT is 0, the counted number will be set to 0000 (D3D2D1D0) when the next clock pulse (rising edge) triggers.

## Slide 84
LD （Rising edge triggered）
0000
0001
0010
0011
0100
0101
0111
1000
1001
1010
0110
1011
Counting Range of Loading Method
When the rising edge triggers, the counted number changes from 1011 to 0000.
It is counting from 0000 to 1011.
Notes: When the rising edge triggers, the counted number changes from 1011 to 0000. It is counting from 0000 to 1011.

## Slide 85: Exercise

## Slide 86
Implement the addition counter ranging from 0000 to 1011 by the loading method.
Notes: D3D2D1D0 is 0000.
If Q3Q2Q1Q0 is 1011, the output of NAND gate is 0.
If LD NOT is 0, the counted number will be set to 0000 (D3D2D1D0) when the next clock pulse (rising edge) triggers.

## Slide 87
CR
CP
Q3 Q2 Q1 Q0
74LS161
CP
Example 2: Implement the addition counter ranging from 0000 to 1011 by the clearing method.
If Q3Q2Q1Q0 is 1100, the output of NAND gate is 0.
If CR NOT is 0, the counted number will be set to 0000 (Q3Q2Q1Q0) at once.
Actually, 1100 (Q3Q2Q1Q0) is invisible.
Notes: If Q3Q2Q1Q0 is 1100, the output of NAND gate is 0.
If CR NOT is 0, the counted number will be set to 0000 at once.
Actually, 1100 (Q3Q2Q1Q0) is invisible.

## Slide 88
1100 （Invisible）
0000
0001
0010
0011
0100
0101
0111
1000
1001
1010
0110
1011
Counting Range of Clearing Method
1100 is invisible.
It is counting from 0000 to 1011.
Notes: 1100 is invisible. It is counting from 0000 to 1011.

## Slide 89: Exercise

## Slide 90
Implement the addition counter ranging from 0000 to 1011 by the clearing method.
Notes: If Q3Q2Q1Q0 is 1100, the output of NAND gate is 0.
If CR NOT is 0, the counted number will be set to 0000 at once.
Actually, 1100 (Q3Q2Q1Q0) is invisible.

## Slide 91: 6.4.2 Register
Example 1:
Design the left shift register of the 3-bit binary codes by J-K flip-flop.
The 3-bit binary code shifts from the lower-bit to the higher-bit.
The 1-bit input variable “X” shifts to the lowest-bit of the binary code.
The 3-bit binary code is the output of the left shift register.

## Slide 92
000
001
010
011
100
101
110
111
0/
1/
0/
1/
1/
0/
0/
1/
0/
1/
0/
1/
0/
1/
0/
1/

## Slide 93
Q3n+1 Q2n+1 Q1n+1
Q3n Q2n Q1n X=0 X=1
0 0 0 0 0 0 0 0 1
0 0 1 0 1 0 0 1 1
0 1 0 1 0 0 1 0 1
0 1 1 1 1 0 1 1 1
1 0 0 0 0 0 0 0 1
1 0 1 0 1 0 0 1 1
1 1 0 1 0 0 1 0 1
1 1 1 1 1 0 1 1 1

## Slide 94
Q3n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
0
0
1
1
1
1
0
1
0
0
0
1
1
0
1
0

## Slide 95
Q2n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
0
1
1
0
0
1
1
1
0
0
1
0
1
1
0
0

## Slide 96
Q1n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
1
1
1
1
1
1
0
0
0
1
1
0
0
0
0
0

## Slide 97
J
Q1
Q1
K
J
Q2
Q2
K
CP
J
Q3
Q3
K
X

## Slide 98
D
Q1
Q1
D
Q2
Q2
CP
D
Q3
Q3
X

## Slide 99
Example 2:
Design the bidirectional shift register of the 2-bit binary codes by D flip-flop.
The shift direction is controlled by the input variable “X1”. And the shift-in number is controlled by the input variable “X2”.
On one hand, if the input variable “X1” is “0”, the register shifts right. That is to say, the 2-bit binary code shifts from the higher-bit to the lower-bit. And the 1-bit input variable “X2” shifts to the highest-bit of the binary code.
On the other hand, if the input variable “X1” is “1”, the register shifts left. That is to say, the 2-bit binary code shifts from the lower-bit to the higher-bit. And the 1-bit input variable “X2” shifts to the lowest-bit of the binary code.
The 2-bit binary code is the output of the bidirectional shift register.

## Slide 100
X1 X2
0 0 （0）
0 1 （1）
1 0 （0）
1 1 （1）

## Slide 101
01
11
10
01
00
10
00
11
11
01
00
01
11
10
00
10
X1 X2
00
11
01
10
X1 X2
0 0 0
0 1 1
1 0 0
1 1 1

## Slide 102
Q2n Q1n X1X2=00 X1X2=01 X1X2=11 X1X2=10
Q2n+1 Q1n+1
00
01
10
11
00
10
11
00
11
00
01
11
10
01
01
10
11
00
10
01
X1X2
0 0 0 0 1 0 0 1 0 0
0 1 0 0 1 0 1 1 1 0
1 0 0 1 1 1 0 1 0 0
1 1 0 1 1 1 1 1 1 0

## Slide 103
Q2n+1
X1X2
Q2nQ1n
00
00
01
01
11
11
10
10
0
1
1
0
0
1
0
0
1
0
1
0
1
1
1
0

## Slide 104
Q1n+1
X1X2
Q2nQ1n
00
00
01
01
11
11
10
10
1
1
1
1
0
0
0
1
0
0
0
1
1
0
1
0

## Slide 105
D
Q2
Q2
D
Q1
Q1
CP
X1
X2

## Slide 106
Example 3: ring counter
D
Q4
Q4
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP

## Slide 107
Q1n+1= Q4n
Q2n+1= Q1n
Q3n+1= Q2n
Q4n+1= Q3n
Q1n Q2n Q3n Q4n Q1n+1 Q2n+1 Q3n+1 Q4n+1
0 0 0 0 0 0 0 0
0 0 0 1 1 0 0 0
0 0 1 0 0 0 0 1
0 0 1 1 1 0 0 1
0 1 0 0 0 0 1 0
0 1 0 1 1 0 1 0
0 1 1 0 0 0 1 1
0 1 1 1 1 0 1 1
（1）:

## Slide 108
Q1n+1= Q4n
Q2n+1= Q1n
Q3n+1= Q2n
Q4n+1= Q3n
Q1n Q2n Q3n Q4n Q1n+1 Q2n+1 Q3n+1 Q4n+1
0 0 0 0 1 0 0
1 0 1 0 0 1 0 1
1 0 1 1 1 1 0 1
1 1 0 0 0 1 1 0
1 1 0 1 1 1 1 0
1 1 1 0 0 1 1 1
1 1 1 1 1 1 1 1
1 0 0 1 1 1 0 0
（2）:

## Slide 109
0000
0001
1000
0100
0010
0011
1001
1100
0110
0111
1011
1101
1110
0101
1010
1111
⑤
④
③
②
①

## Slide 110
0001
1000
0100
0010
It is not self-starting.
N flip-flops,
N valid states
ring counter
D
Q4
Q4
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP

## Slide 111
D
Q4
Q4
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP

## Slide 112
Q1n Q2n Q3n Q4n D1
0 0 0 0 1
0 0 0 1 1
0 0 1 0 0
0 0 1 1 0
1 1 1 0 0
1 1 1 1 0
0011
1001
1100
0110
0101
1010
0000
1111
1011
0111
1101
1110
0 1 0 1 0
⑤
④
③
②
①
Valid cycle

## Slide 113
D1
Q1nQ2n
Q3nQ4n
00
00
01
01
11
11
10
10
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
1

## Slide 114
D
Q4
Q4
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP
It is self-starting.

## Slide 115
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP
Example 4: twisted-ring counter

## Slide 116
Q1n Q2n Q3n Q1n+1 Q2n+1 Q3n+1
0 0 0 1 0 0
0 0 1 0 0 0
0 1 0 1 0 1
0 1 1 0 0 1
1 0 0 1 1 0
1 0 1 0 1 0
1 1 0 1 1 1
1 1 1 0 1 1

## Slide 117
Q1n Q2n Q3n Q1n+1 Q2n+1 Q3n+1
0 0 0 1 0 0
0 0 1 0 0 0
0 1 0 1 0 1
0 1 1 0 0 1
1 0 0 1 1 0
1 0 1 0 1 0
1 1 0 1 1 1
1 1 1 0 1 1
000
100
110
111
011
001
101
010
Invalid cycle
Valid cycle

## Slide 118
000
100
110
111
011
001
Valid cycle
It is not self-starting.
N flip-flops, 2N valid states
twisted-ring counter
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP

## Slide 119
Q1n Q2n Q3n Q1n+1 Q2n+1 Q3n+1 D1 D2 D3
0 0 0 1 0 0 1 0 0
0 0 1 0 0 0 0 0 0
0 1 0 1 0 1 0 0 1
0 1 1 0 0 1 0 0 1
1 0 0 1 1 0 1 1 0
1 0 1 0 1 0 0 1 0
1 1 0 1 1 1 1 1 1
1 1 1 0 1 1 0 1 1
101
010
Invalid cycle

## Slide 120
Q1n Q2n Q3n Q1n+1 Q2n+1 Q3n+1 D1 D2 D3
0 0 0 1 0 0 1 0 0
0 0 1 0 0 0 0 0 0
0 1 0 1 0 1 0 0 1
0 1 1 0 0 1 0 0 1
1 0 0 1 1 0 1 1 0
1 0 1 0 1 0 0 1 0
1 1 0 1 1 1 1 1 1
1 1 1 0 1 1 0 1 1

## Slide 121
Q1n
Q2nQ3n
00
01
11
10
0
1
1
0
0
1
0
0
1
0
D1
D
Q3
Q3
D
Q2
Q2
D
Q1
Q1
CP

## Slide 122
D
Q2
Q2
D
Q1
Q1
D
Q0
Q0
CP
Example 5: Maximum Length Shift-Register Counter

## Slide 123
Q0n Q1n Q2n Q0n+1 Q1n+1 Q2n+1
0 0 0 0 0 0
0 0 1 1 0 0
0 1 0 1 0 1
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 1 1 1
1 1 1 0 1 1

## Slide 124
011
111
110
101
010
100
001
000
Valid cycle
Q0n Q1n Q2n Q0n+1 Q1n+1 Q2n+1
0 0 0 0 0 0
0 0 1 1 0 0
0 1 0 1 0 1
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 1 1 1
1 1 1 0 1 1
n flip-flops, N=2n-1 valid states

## Slide 125
Q0n Q1n Q2n Q0n+1 Q1n+1 Q2n+1
0 0 0 1 0 0
0 0 1 1 0 0
0 1 0 1 0 1
0 1 1 0 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 1 1 1
1 1 1 0 1 1

## Slide 126
Q0n
Q1nQ2n
00
01
11
10
0
1
1
0
1
1
1
1
0
0
Q0n+1

## Slide 127
D
Q2
Q2
D
Q1
Q1
D
Q0
Q0
CP

## Slide 128: 6.4.3 Integrated Bidirectional Shift Register
1
8
9
16
74LS194
D0
VCC
Q3
Q1
Q2
Q0
M1
D3
D1
D2
DSL
CP
CR
M0
DSR

## Slide 129
D0、D1、D2、D3 ：input data
CR：reset to“0”
CP：clock pulse (rising-edge triggered)
1
8
9
16
74LS194
D0
VCC
Q3
Q1
Q2
Q0
M1
D3
D1
D2
DSL
CP
CR
M0
DSR

## Slide 130
Q0、Q1、Q2、Q3：shifted binary code
1
8
9
16
74LS194
D0
VCC
Q3
Q1
Q2
Q0
M1
D3
D1
D2
DSL
CP
CR
M0
DSR
DSR,DSL：input data for right or left shift
M1、M0：working mode （01 right shift，10 left shift，11 loading data，00 keeping）

## Slide 131
0 d d d d d d d d d 0 0 0 0
CR M1 M0 DSR DSL CP D0 D1 D2 D3
1 0 1 0 d d d d d 0
1 0 1 1 d d d d d 1
1 d d d d 0 d d d d
1 1 0 d 1 d d d d 1
1 1 0 d 0 d d d d 0
1 0 0 d d d d d d d
1 1 1 d d d0 d1 d2 d3 d0 d1 d2 d3
reset
no rising-edge
loading
keeping
1
0
1
0
M1、M0：working mode （01 right shift，10 left shift，11 loading data，00 keeping）

## Slide 132
Q0Q1Q2Q3
1100 0110 0011 1001
M1M0=11,loading data“1100”. M1M0=01,right shift.
CP
D0 D1 D2 D3
Q0 Q1 Q2 Q3
74LS194
CP
DSR
M1
M0
“1”
control
Example: Design a counter for the following four numbers by the integrated register 74LS194.

## Slide 133: 6.4.4 Sequence Generator
Example: Design the sequence generator (11110000) by J-K flip-flop.
Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
0 0 0 0 0 1 1
0 0 1 0 1 0 1
0 1 0 0 1 1 1
0 1 1 1 0 0 1
1 0 0 1 0 1 0
1 0 1 1 1 0 0
1 1 0 1 1 1 0
1 1 1 0 0 0 0
1. State Transition Table
Notes: The sequence generator has 8 bits. The first generated bit is 1. The last generated bit is 0.
Each bit is generated by state transition. So we have 8 state transitions.
We have 8 lines in state transition table. The states are from 000 to 111.
When state 000 changes into 001, the first bit is generated. So at this time circuit output Z is 1.
We write Q3 on the far left. Because Q3 is the highest bit.

## Slide 134
The sequence generator has 8 bits.
The first generated bit is 1.
The last generated bit is 0.
Each bit is generated by state transition.
So we have 8 state transitions.
We have 8 lines in state transition table.
The states are from 000 to 111.

## Slide 135
Q3n
Q2nQ1n
00
01
11
10
0
1
1
0
1
1
0
0
0
1
Q3n+1
Q2nQ1n
00
01
11
10
0
1
0
0
1
1
1
1
0
0
Q2n+1
Q3n
2. Simplification by K-map
J-K Flip-Flop:
Notes: The circuit is required to be implemented by JK flip-flop.
Look at the K-map of Q3’s next state equation.
We draw K-circles in shadow blocks to get Q3’s current state inverter.
We draw K-circles in clear blocks to get Q3’s current state.

## Slide 136
Q2nQ1n
00
01
11
10
0
1
0
1
1
1
0
1
0
0
Q1n+1
Q2nQ1n
00
01
11
10
0
1
1
1
0
0
1
1
0
0
Z
Q3n
Q3n
J-K Flip-Flop:

## Slide 137
J1
Q1
Q1
K1
J2
Q2
Q2
K2
J3
Q3
Q3
K3
CP
Z
1
3. Circuit Diagram

## Slide 138: Exercise

## Slide 139
Design the sequence generator (11110000) by J-K flip-flop.
Notes: The sequence generator has 8 bits. The first generated bit is 1. The last generated bit is 0.
Each bit is generated by state transition. So we have 8 state transitions.
We have 8 lines in state transition table. The states are from 000 to 111.
When state 000 changes into 001, the first bit is generated. So at this time circuit output Z is 1.
We write Q3 on the far left. Because Q3 is the highest bit.

## Slide 140: 6.4.5 Sequence Detector
X：0110111111101011110101
Y：0000001111100000110000
Example: Design an overlapped “111” sequence detector with J-K Flip-Flop.
The last two “1s” in the previous sequence can be reused by the current sequence.
Notes: The last“1” in the previous sequence can be reused by the current sequence.

## Slide 141
S0: There is no “1”.
S1: There is a single “1”.
S2: There are two “1s”.
1. Define States for Sequence Detector
We are required to detect the overlapped “111” sequence.
There are 3 bits in the sequence.
So we need to define 3 states only.
Notes: We are required to detect the overlapped “111” sequence.
There 3 bits in the sequence.
So we need to define 3 states only.

## Slide 142
S0
S1
S2
1/0
0/0
1/0
0/0
0/0
1/1
2. State Transition Diagram (before assigning the code)
S0S1: The input sequence is “1”.
S1S2: The input sequence is “11”.
S2S2: The input sequence is “111”. The output becomes 1.
Invalid Sequence:
S0S0: “0”
S1S0: “10”
S2S0: “110”
Notes: S0S1: The input sequence is “1”. S0 changes into S1.
S1S2: The input sequence is “11”.
S2S2: The input sequence is “111”. The output becomes 1.
S0S0: the input sequence is “0”. The current state is S0. The next state is also S0.
S1S0: the input sequence is “10”.
S2S0: the input sequence is “110”.

## Slide 143
S0=00 S1=01 S2=10 S3=11(unused state)
00
01
10
1/0
0/0
1/0
0/0
0/0
1/1
2. State Transition Diagram (after assigning the code)
Assign codes to states with two-bit binary numbers in the ascending order.
S3 is the unused state. But we need it in state transition table.
Notes: Assign codes to states by two-bit binary numbers in the ascending order.
S0 is 00. S1 is 01. S2 is 10. S3 is 11.
S3 is the unused state. But we need it in state transition table.

## Slide 144
S0=00 S1=01 S2=10 S3=11(unused state)
X Q1n Q0n Q1n+1 Q0n+1 Y
0 0 0 0 0 0
0 0 1 0 0 0
0 1 0 0 0 0
0 1 1 d d d
1 0 0 0 1 0
1 0 1 1 0 0
1 1 0 1 0 1
1 1 1 d d d
00
01
10
1/0
0/0
1/0
0/0
0/0
1/1
3. State Transition Table
Notes: Convert state transition diagram into state transition table.
Look at state transition table. We have circuit input X, current state, next state, circuit output Y.
We write Q3 on the far left. Because Q3 is the highest bit.
Look at the first line. State 00 is unchanged, when the input bit X is 0. At the same time, circuit output Y is 0.
The next state of S3 is “d”(don’t care term). The output of S3 is “d”(don’t care term.)

## Slide 145
S3 is the unused state. But we need it in state transition table.
The next state of S3 is “d”(don’t care term).
The output of S3 is “d”(don’t care term.)

## Slide 146
X
Q1nQ0n
00
01
11
10
0
1
0
d
1
1
0
0
0
d
Q1n+1
X
Q1nQ0n
00
01
11
10
0
1
0
d
0
0
0
0
1
d
Q0n+1
4. Simplification by K-map
J-K Flip-Flop:
Notes: Simplify state equation by K-map.
The circuit is required to be implemented by JK flip-flop.
Look at the K-map of Q1’s next state equation.
We draw K-circles in shadow blocks to get Q1’s current state inverter.
We draw K-circles in clear blocks to get Q1’s current state.
Look at the state equation of Q0. We don’t have Q0’s current state. So K0 is 1.

## Slide 147
X
Q1nQ0n
00
01
11
10
0
1
0
d
0
1
0
0
0
d
Y
Draw K-circle on “1” blocks only. Otherwise, the output Z will be wrong.
It is self-starting.
0 1 1 0 0 0
1 1 1 1 0 0
X Q1n Q0n Q1n+1 Q0n+1 Y
Notes: Simplify output equation by K-map.
Draw K-circle on “1” blocks only. Otherwise, the output Z will be wrong.

## Slide 148
J0
Q0
Q0
K0
J1
Q1
Q1
K1
CP
X
Y
5. Circuit Diagram

## Slide 149: Exercise

## Slide 150
Design an overlapped “111” sequence detector with J-K Flip-Flop.
Notes: The last“1” in the previous sequence can be reused by the current sequence.

## Slide 151: 6.4.6 Code Detector
Example: Design the “011” code detector with D flip-flop.
The input code is entered from the highest bit to the lowest bit.
If the input is “011”, the output is “1”. Otherwise, the output is “0”.
The circuit returns to the initial state after the input of each code.

## Slide 152
1/1
0/0
A
B
0/0
C
1/0
D
0/0
E
1/0
F
0/0
G
1/0
1/0
0/0
0/0
1/0
0/0
1/0
1. State Transition Diagram
The code “011” is detected. The circuit output becomes 1.
The circuit returns to the initial state after the input of each code.
Notes: The code “011” is detected. The circuit output becomes 1.
The circuit returns to the initial state after the input of each code.

## Slide 153
A
B
0/0
C
1/0
D
0/0
E
1/0
F
0/0
G
1/0
0/0
1/0
0/0
1/1
0/0
1/0
0/0
1/0
D, F and G are equivalent states.
Find Equivalent States
They have the same input-output pair (0/0, 1/0).
They have the same next state (“A”).
Notes: They have the same input-output pair (0/0, 1/0). They have the same next state (“A”).

## Slide 154
D
A
B
C
0/0
1/0
E
0/0
1/0
0/0
1/0
0/0
1/1
0/0
1/0
A
B
0/0
C
1/0
D
0/0
E
1/0
F
0/0
G
1/0
0/0
1/0
0/0
1/1
0/0
1/0
0/0
1/0
Leave out state F and state G.
Remove Equivalent States
The next state of “C” is changed into “D”.
Notes: The next state of “C” is changed into “D”.

## Slide 155
A B C D E
000 001 010 011
100
011
000
001
010
0/0
0/0
1/0
0/0
1/0
0/0
1/1
100
0/0
1/0
1/0
D
A
B
C
0/0
1/0
E
0/0
1/0
0/0
1/0
0/0
1/1
0/0
1/0
Assign codes to the states with 3-bit binary numbers in the ascending order.
Notes: Assign codes to the states by 3-bit binary numbers in the ascending order.

## Slide 156
X Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
000
010
001
100
011
0/0
1/0
0/0
0/0
0/0
1/0
1/0
1/1
0/0
1/0
0 0 0 0 0 0 1 0
0 0 0 1 0 1 1 0
0 0 1 0 0 1 1 0
0 0 1 1 0 0 0 0
0 1 0 0 0 0 0 0
0 1 0 1 d d d d
0 1 1 0 d d d d
0 1 1 1 d d d d
2. State Transition Table (first half)
Notes: Look at state transition table.
We have circuit input X, current state, next state, circuit output Z.
We write Q3 on the far left. Because Q3 is the highest bit.
Look at the fist line.
When the circuit input X is 0, state 000 changes into 001. At the same time, the circuit output Z is 0.
Look at the unused state 101.
Its next state is “d”(don’t care term). Its output is “d”(don’t care term).

## Slide 157
X Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
000
010
001
100
011
0/0
1/0
0/0
0/0
0/0
1/0
1/0
1/1
0/0
1/0
1 0 0 0 0 1 0 0
1 0 0 1 1 0 0 0
1 0 1 0 0 1 1 0
1 0 1 1 0 0 0 0
1 1 0 0 0 0 0 1
1 1 0 1 d d d d
1 1 1 0 d d d d
1 1 1 1 d d d d
2. State Transition Table (second half)

## Slide 158
Q3n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
0
d
d
d
0
0
0
0
0
0
1
0
d
d
d
0
3. Simplification by K-map
The circuit is required to be implemented by D flip-flop.
Characteristic Equation of D Flip-Flop:
Notes: The circuit is required to be implemented by D flip-flop.

## Slide 159
Q2n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
0
d
d
d
1
0
1
0
0
1
0
1
d
d
d
0
Characteristic Equation of D Flip-Flop:

## Slide 160
Q1n+1
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
0
d
d
d
1
0
1
0
0
0
0
1
d
d
d
1
Characteristic Equation of D Flip-Flop:

## Slide 161: .
Z
XQ3n
Q2nQ1n
00
00
01
01
11
11
10
10
1
d
d
d
0
0
0
0
0
0
0
0
d
d
d
0
Draw K-circle on “1” blocks only. Otherwise, the output Z will be wrong.

## Slide 162
X Q3n Q2n Q1n Q3n+1 Q2n+1 Q1n+1 Z
0 1 0 1 0 1 0 0
0 1 1 0 0 1 1 0
0 1 1 1 0 0 0 0
1 1 0 1 1 0 0 0
1 1 1 0 0 1 1 0
1 1 1 1 0 0 0 0
It is self-starting. No output error.

## Slide 163
Can you draw the circuit diagram?
Use three D flip-flops

## Slide 164: Exercise

## Slide 165
Design the “011” code detector with D flip-flop.
The input code is entered from the highest bit to the lowest bit.
If the input is “011”, the output is “1”. Otherwise, the output is “0”.
The circuit returns to the initial state after the input of each code.